## Slide 1: Jelly Roll
Notes: You can use the heading from the application documentation for the title.

## Slide 2: Background
In a cylindrical or prismatic battery cell, the active layers, current collector metal foils and separators are wound into a “jelly roll”
Additional tabs (metal strips) are welded to the current collector foils in order to conduct the current to the exterior of the cell can
The interplay of the various dimensions of the layers and the tabs, in combination with the magnitude of the cell current, governs the temperature and current distribution in the battery cell
This tutorial models the ohmic and activation losses, and the resulting temperature distribution, in a jelly roll for a pseudo-stationary case at a constant cell current

## Slide 3: Jelly Roll Configuration
Positive Current Collector
Positive Electrode Layer
Separator
Negative Electrode Layer
Negative Current Collector
Negative Electrode Layer
Separator
Positive Electrode Layer
Positive Tab
Negative Tab
Positive Tab

## Slide 4: Model Geometry
The model is defined in 3D
The roll is designed to fit a 18650 can
  60 mm high
  8.5 mm outer spiral radius, including negative tab
  2 mm inner radius, including positive tab
Parametric curves, based on archimedal spiral functions are used to define the winding
  A constant cell thickness is assumed
The geometry is finalized as an assembly of two parts
  Assembly boundaries are placed in the middle of the separators
  This allows for sweeping the meshes in the thru-plane direction
Positive Tab

## Slide 5: Materials
Positive Tab
  Aluminum, 100 mm thick, 4 mm wide
Positive Current Collector
  Aluminum, 10 mm thick
Positive Electrode
  NMC 111, 200 mm thick
Separator
  30 mm thick
Negative Electrode
  Graphite, 200 mm thick
Negative Current Collector
  Copper, 10 mm thick
Negative Tab
  Nickel, 100 mm thick, 4 mm wide
Material nodes in the model builder

## Slide 6: Physics Definition
Secondary Current Distribution
  Defines the pseudo-stationary operation point for a constant current
  Includes ohmic resistances and activation polarization (no concentration effects included)
  Cell current of 3 A applied at the positive terminal
  Negative terminal is grounded
Heat Transfer in Solids
  Convective heat flux condition on the outer jelly roll boundary facing the can
Electrochemical Heating
  Heat sources added due to ohmic resistances (Joule heating) and activation overpotentials
Physics setup in the model builder

## Slide 7: Electrode Phase Polarization
Negative Side
Positive Side

## Slide 8: Temperature