## Slide 1: Extracting Electrical Circuits from Electromagnetic Simulations

## Slide 2: Highlights
Circuit Extractor add-in
  Basics and preliminary steps
  Primer on Circuit Extractor, introductory case
  RL square wave response verification, case 1
  Resistors network stationary current verification, case 2
  RLC frequency domain extraction for PCB coil model, case 3
More information in blog Extracting Electrical Circuits from Electromagnetic Simulations
Models available here

## Slide 3: Circuit Extractor Add-in, Basic & Preliminary Steps
Convert Source Sweep studies into Electrical Circuits
Click on "Developer" in top ribbon
Select "Add-in Libraries“
Expand the AC/DC Module
Check "circuit_extractor"

## Slide 4: Primer on Circuit Extractor
Open model for introductory case with suffix “BeforeAddin”
Solve Source Sweep, getting lumped matrices
From Developer menu, Add-ins, select “Circuit Extractor”
Set Circuit Extractor as in image and press “Extract Circuit”
Output
SPICE File Preview
Electrical Circuit Interface
.cir file

## Slide 5: CASE 1: RL Square Wave Response Verification
Self inductance smooths resulting current as because of as self inductance RL response
Mutual inductive effects will generate currents on secondary coil
Input square voltage signal on previous example
Solid line: full FEM transient approach, solved by means of "Magnetic Fields" physics
Open circles: solving the extracted Electrical Circuit
Comparison of FEM and CIR

## Slide 6: CASE 2: Resistors Network Stationary Current Verification
Geometry from ECAD Import Module Library. The ODB++ file is provided courtesy of Hypertherm, Inc., Hanover, NH, USA
Extract circuit of a 6 pin resistive mix feeding network

## Slide 7: CASE 3: RLC Frequency Domain Extraction for PCB Coil Model
Matrices from different physics
Extracting single RLC and sweeping regimes from inductive to capacitive
Model computing separately RL and C
Impedance showing LC resonance
Power transfer for different lines
Frequency sweep of extracted circuit