## Slide 1: Water and Carbon Dioxide Co-Electrolysis in a Solid Oxide Electrolyzer Cell
COMSOL

## Slide 2: Overview
A solid oxide electrolyzer cell model is presented here for co-electrolysis of H2O and CO2
The model includes the full coupling between the mass balances and gas flow in the H2 and O2 gas diffusion electrodes, the momentum balances in the H2 and O2 gas flow channels, the energy balance across the cell, the balance of the ionic current carried by the oxide ion, and an electronic-current balance
A reversible water gas shift reaction is included in the H2 gas diffusion electrode and H2 gas flow channel
The model computes the spatial distributions of the various species across the gas diffusion electrodes and gas flow channels
The spatial distribution of the total current density along the electrode length is also evaluated in the model using the general projection operator

## Slide 3: Model Geometry
Membrane
Gas Diffusion Electrode
Gas Flow Channel
Gas Flow Channel
Interconnect
Interconnect
Geometry defined in 2D
  Includes gas diffusion electrode, gas flow channel and interconnect for the anode and cathode in addition to membrane
The modeled species in H2 Gas Mixture (Cathode): H2, H2O, CO2 and CO
The modeled species in O2 Gas Mixture (Anode): O2 and N2
Gas Diffusion Electrode

## Slide 4: Model Definition
H2O electrolysis reaction occurs at the H2 gas diffusion electrode
  2H2O(g) + 4e- → 2H2(g) + 2O2-
CO2 electrolysis reaction occurs at the H2 gas diffusion electrode
  CO2(g) + 2e- → CO (g) + O2-
Oxygen ions are oxidized to form oxygen gas at the O2 gas diffusion electrode
  2O2- → O2(g) + 4e-
A reversible water gas shift reaction occurs at the H2 gas diffusion electrode and H2 gas flow channel
  CO(g) + H2O(g) CO2(g) + H2(g)

## Slide 5: H2 and CO Concentrations
H2 and CO concentrations are found to increase along the electrode length due to H2O and CO2 electrolysis reactions, respectively, for applied potential of 1.5 V
Difference in concentration between the H2 gas diffusion electrode and H2 gas flow channel is considerably higher for CO when compared to H2, which is attributed to slower diffusion of CO than H2
H2 concentration at applied potential = 1.5 V
CO concentration at applied potential = 1.5 V

## Slide 6: Water Gas Shift Reaction Rate and Temperature
The rate of water gas shift reaction is found to be higher closer to the H2 gas diffusion electrode-membrane interface for applied potential of 1.5 V, which is attributed to the high CO concentration in the region
Although both H2O and CO2 electrolysis reactions are endothermic, the cell temperature is increased by about 25 K from inlet to outlet for applied potential of 1.5 V. As this applied potential is higher than the thermoneutral potential for both H2O and CO2 electrolysis reactions, the heat generated from overpotential losses is more than the heat required for electrolysis reactions.
Water gas shift reaction rate at applied potential = 1.5 V
Change in temperature at applied potential = 1.5 V

## Slide 7: Total Current Density
The total cathodic (negative) current density, which is integrated along the y-direction for each grid point along the x-direction using the general projection operator, is found to decrease for H2O electrolysis and to increase for CO2 electrolysis, along the electrode length
Total current density at applied potential = 1.5 V

## Slide 8: References
M. Ni, “2D thermal modeling of a solid oxide electrolyzer cell (SOEC) for syngas production by H2O/CO2 co-electrolysis”, International Journal of Hydrogen Energy, Vol. 32, pp. 6389-6399 (2012)