## Slide 1: Battery Cell Anomaly Detection via IAV Virtual Battery Testbench based on COMSOL® API
COMSOL Conference Florence 2024
Dr. Johannes Werfel, Dr. Reik Laubenstein, Dr. Jakob Hilgert, Dr. Maria Kalogirou

## Slide 2
IAV Battery Development
Over > 1,000 EV & battery specialists
Providing tech solutions worldwide at 24 locations
  More then 30 years of experience in EV & battery development
Concept
Development
Serial
Development
Integration & Calibration
SoP
EoL
Fast Charging
Thermal Management
BMS HW & SW using AI
New Cell Chemistries
Simulation

## Slide 3: Virtual Development
Simulation Environment
FMU
virtual Battery Testbench
OIIOI
Other Models
Virtual development is the key to achieve the needed reduction of time and costs for the development of electric vehicles
    Battery expert
    Broad expertise in battery cell modelling
    Model distribution to specialists in other fields
    Uses COMSOL Multiphysics® and COMSOL CompilerTM
    Other models (e.g., GT AutolionTM, PyBAMM) can also be used
    BMS / thermal management / vehicle experts
    Can run parallel calculations within their usual tool chains and developing environments (e.g., INCA-FLOWTM, GT-SUITETM, SIMULINK® etc.) without the need of a COMSOL license.
API
Probes
COMSOL APP
COMSOL Cell Model
FMU: Functional Mock-Up Unit API: Application Programming Interface SOC / SOH: State of Charge / Health

## Slide 4: Timeline for Thermal Runaway and Propagation
Production
  Controlling of process, material and final product. Elimination of faulty or problematic cells through quality management.
Early Detection
  Internal changes and strange behavior of cell voltage during idle and runtime. External signals usually undetectable.
Propagation
  Heat generation during thermal runaway high enough to propagate on neighboring cells. Only drastic solutions capable to prevent spreading or damp event.
Detection
  Detection of increased temperature (internal and/or external). After Point of no return exothermic reactions exceed cooling capacity.
Early detection of cell anomaly supports preventing catastrophic battery scenarios
seconds
minutes
days
years
months
hours

## Slide 5: Anomaly Detection – Overview Approach
Driving profile
Cell model
Cell model
Cell model
Cell model 1
    Healthy cell Faulty cell
BMS with algorithm
ECU
Battery
u, i
    Simulink
    COMSOL
    Simulink
Fault detection
Boundary conditions
Fault diagnosis methods
Analytic model based
Signal processing based
Knowledge based
Neural networks
Fuzzy logic
Machine learning
Random forest
Entropy
Correlation analysis
Transformation
Wavelet
Fourier
Correlation coefficient
Shannon
State estimation
Parity space
Parameter estimation
Recursive least squares
Filter
Kalman filters
Luenberger observer
Nonlinear parity equations
Balancing
    The cell model is abstracted to JAVA code and compiled into a COMSOL App
    Balancing function applies shunt to corresponding cell
Noise & Quantization

## Slide 6: Anomaly Detection – Overview Input
    Model set-up
    Current profile contains idle, driving and charging phases
    12 cells, NMC811 chemistry, 12s1p configuration, 78 Ah, initial SOC 80%
    Cell models in COMSOL APP feature adjustable statistical differences in capacity and state of aging
    Variation of cell parameters:
      Healthy cells Risc either 10,000 or 1,000,000 Ω; faulty cell Risc is 100 Ω (●)
      Cell capacity scales between ± 2%
      Cell film resistance scales between ± 5%
SOC: State of Charge Risc: resistance of the internal short circuit
Voltage signals of cells with varying RISC not distinguishable without application of algorithms

## Slide 7: Anomaly Detection – Recursive Least Squares Method
    Parameter estimation of Duocv and Dri to minimize error between linear mean difference model (difference of each cell to mean value) and measured values
Parameter estimation depends on input (dynamic or steady state operation point)
Battery System
Mean Difference Model
Parameter Estimation
error
input
output

## Slide 8: Anomaly Detection – Recursive Least Squares Method
    Results
    Estimated parameter of Dui and Dri for all 12 cells are shown
    Dri: cells with high and low capacities (● ● ●) detectable as outliers
      Small influence of the low Risc (100 Ω) for the faulty cell (●)
    Duocv: cells with high & low capacities (● ● ●) and faulty cell (●) detectable as outliers
    Continues self discharge due to low Risc for faulty cell detectable as permanent deviation of measured and estimated Docv value (●)

## Slide 9: Anomaly Detection – Random Forest Classification Method
Accuracy depends on the definition and extraction of features.
Classification with trained model
Training data set
Feature extraction
Training of RF model
Test data set
Model parameters
Result
Selected Features:
Energy loss during discharge and charge cycle
Change in equivalent resistance of the cell
Voltage drop during idle time
Input data set with n features
Tree 1
Tree 2
Tree m
…
Final class through majority voting
Each tree uses a subset of n features

## Slide 10: Anomaly Detection – Random Forest Classification Method
    Adjustment of set-up (COMSOL model)
    Input of 52 cells  Adjustment of the model to increase number of cells
    RISC values of 100, 1,000 and 10,000 Ohm examined
    From available data 75% used for training, 25% as test data
    Results
    Detection of faulty cells with low internal short circuit resistance (100 Ohm) mostly correctly classified
Despite small size of training data set, good accuracy for identification of faulty cells
State of cell | Healthy | Unhealthy
Accuracy on test samples | 87.5% (7/8) | 80% (4/5)

## Slide 11: Summary & Outlook
    Model-based approaches are the key to achieve the needed reduction of time and costs in the development process of electric vehicles
    IAV has established a holistic virtual development process for batteries using COMSOL Application Builder in conjunction with COMSOL CompilerTM
    The exemplary use-case of cell anomaly detection development was presented
      Identification of cells with a low internal short circuit resistance via BMS-available signals
      Signals of faulty and healthy cells were generated via cell models
      Two different fault detection algorithms with different approaches were selected and compared (a third one is shown on the poster)
Computational cost
Accuracy
Recursive Least Square
Random Forest

## Slide 12
Dr. Johannes Werfel
IAV GmbH
Carnotstraße 1, 10587 Berlin, GERMANY
Phone +49 152 56408750
johannes.werfel@iav.de
www.iav.com
electrified by vision

## Slide 13: Backup

## Slide 14: Anomaly Detection – Shannon Entropy Method
    Weight factor of entropy (green / S yellow)
    Score for each cell is entropy times weight factor
    Difference score of each cell to mean value
    Probability p of each cell i at each sampling point j
    Entropy h at each sampling point
moving window 
m
s
-s
-2s
2s
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
std | 0.0015831 | 0.0027166 | 0.0044789 | 0.0070949 | 0.010798 | 0.01579 | 0.022184 | 0.029945 | 0.038837 | 0.048394 | 0.057938 | 0.066645 | 0.073654 | 0.078209 | 0.079788 | 0.078209 | 0.073654 | 0.066645 | 0.057938 | 0.048394 | 0.038837 | 0.029945 | 0.022184 | 0.01579 | 0.010798 | 0.0070949 | 0.0044789 | 0.0027166 | 0.0015831
Accuracy depends on selected sampling frequency and size of window

## Slide 15: Anomaly Detection – Shannon Entropy Method
    Results
    High difference score for cells with high and low capacities (● ● ●) during driving phase
    Specifically during idle and charging phases the damaged cell (●) difference score on high level or increasing
    Extension of idle phase leads to permanent increasing difference score for the faulty cell
Faulty cell behavior pre-dominantly visible during idle phase

## Slide 16: Application Examples
Novel Battery Concept with an Innovative Thermal Management*
* More details at “IAV’s multi-purpose 3D coupling solution for electrophysicochemical Battery models via COMSOL-API”, COMSOL Conference Munich 2023 ** More details at “Early Fault Detection in Lithium-Ion Batteries with Smart BMs”, 41st International Battery Seminar, 2024.​ .​
Early Cell Anomaly Detection with BMS-accessible Signals**
BMS
Algorithm
Simulation Environment
FMU
virtual Battery Testbench
OIIOI
Other Models
API
Probes
COMSOL APP
COMSOL Cell Model

## Slide 17: Thermal Runaway & Propagation – The Battery plays Domino
Causes
Mechanisms
Degradation modes
Thermal runaway
Thermal propagation
    Low temperature charging
    Contamination and defect
    Local mechanical deformation
    Overheating
    Overcurrent
    Overcharge
    Over-discharge
    Electrolyte degradation
    Separator degradation
    Dendrites
    Electrolyte degradation
    Solid electrolyte interphase degradation
    Electrode degradation
    Short-circuit
    Exothermic self-heating
    Cell level
    Module level
    Pack level

## Slide 18: Internal Short Circuit
R0
OCV
R1
C1
iload
Cu current collector
SEI
Al current collector
Electrolyte
Separator
Interphase
Anode
Cathode
Discharge
Charge
Li+
Li+
Li+
Li+
Internal short circuit can be modelled as a parallel resistor in the equivalent circuit
Risc
iisc
i0
Electrical equivalent model:
Modelling of low frequency behavior
No electro-chemical process

## Slide 19: Shannon Entropy Method – 10 Ohm Risc

## Slide 20: Shannon Entropy Method – 50 Ohm Risc

## Slide 21: Shannon Entropy Method – 100 Ohm Risc