## Slide 1
A comprehensive COMSOL Modeling for the solar-driven CO2 electroreduction to CO
Matteo Agliuzza1, Candido Fabrizio Pirri1,2, Adriano Sacco2
1Applied Science and Technology Department, Polytechnic University of Turin, Corso Duca degli Abruzzi 24, 10129 Torino, Italy
2Center for Sustainable Future Technologies @Polito, Italian Institute of Technology, Corso Trento 21, 10129 Torino, Italy
matteo.agliuzza@polito.it
Matteo Agliuzza
Ph.D. Candidate
Supervisors: Prof. Candido Fabrizio PIRRI and Adriano SACCO

## Slide 2
Introduction
Circular economy and CO2RR
Artificial Leaf
Introduction on the existing device and results
COMSOL Model
Mathematical model for the physical study of the electrochemical reactor.
Conclusions
Conclusions and brief hint about the perspectives of the future works
Outline
1

## Slide 3
Carbon Neutral cycle
CO2 reactor
Emissions from
combustion
CO2
Fuels
Chemicals
Renewable
Energy Sources
Introduction
2
Positive net balance of carbon in atmosphere
Carbon neutrality achieved by the transformation of into valuable products, such as, Carbon monoxide (), Formic Acid (). Methanol (), Methane (),Ethylene () …

## Slide 4
Introduction
3
Anode
OER
Cathode
[…]
CO2RR
HER
Ag
Sn-Cu
Cu
Zeng et al, Catalysts 2021

## Slide 5
Artificial Leaf project
4
Sacco et al, Sust. Chem. Eng. 2020
Dye-sensitized solar cells
Pt cathode
TiO2 photo-anode
Electrolytic batch cell
Ag NPs cathode
Pt anode
Overall Reactions
Anode:
Cathode:
Solar cell
(DSSC)
Electrolytic cell
Shared electrode

## Slide 6
COMSOL Simulation: WHY?
5
Lead the scaling-up process of the electrochemical reactor
Predict chemical conditions in:
- boundary layers at interfaces
- bulk
Predict performance of the device
Before prediction, the model is validated through experimental results

## Slide 7
Inlet (CO2 - saturated 0.1M KHCO3)
Inlet (CO2 - saturated 0.1M KHCO3)
Outlet
Outlet
Anode (Pt)
Cathode (Ag)
O2
H2O
CO
CO2
H+
BL
BL
Membrane
H+
CO2
K+
OH-
HCO3
-
CO3
2-
O2
H+
CO2
K+
OH-
HCO3
-
CO3
2-
CO
H2
Ф = 0
Ф = -Vc
Фm = Фe - ΔФd
Фm = Фe - ΔФd
x
y
x=xa
x=xa
xa
xm
xc
x=xm
x=xm
0
0
H
L
L
Lm
x=xa
x=xa
Recirculation through inlets/outlets
Membrane is implemented as fixed space charge
Stationary conditions are investigated
EC Model: highlights
2D model
All products and species remain in liquid phase
Catalysts are simulated through their kinetic parameters
System is isothermal @ ambient T°
Assumptions
Agliuzza et al, J. Phys. Energy (2024)
6

## Slide 8
Model: main equations
7

## Slide 9
Anode – Cathode domains
8
Current distribution
Equilibrium reactions
Nernst-Planck Equation:
diffusion
migration
convection
+
Tertiary Current Distribution (TCD) – Electrochemistry module
Inflows/Outflows

## Slide 10
Anode – Cathode boundaries
9
Tertiary Current Distribution (TCD) – Electrochemistry module
Electrochemical reactions
Kinetics
Butler-Volmer Equation:
CO2RR
HER
OER

## Slide 11
Membrane Domain
Secondary Current Distribution (CD) – Electrochemistry module
Ohm’s Law
No significant concentration gradients are expected in the membrane
Donnan potential
Required to let TCD and CD interfaces interact
10

## Slide 12
Results #1: Cell length L
L=0.6 cm
L=0.25 cm
11
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 13
Solar-driven CO2 reduction: Experiment
Operational Point
Power matching requires a suitable match between the voltage-current points of both PV and EC modules.
The PV is made of a module of 6 Dye-Sensitized Solar Cells
Iop=8.6 mA (approx. 3.4 mA/cm2)
Vop=3.1 V
FEco = 82% , FEH2 = 18%
op
op
12
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 14
13
Solar-driven CO2 reduction: Model
Step 1: Define the mathematical model for the solar cell
Step 2: Fit the experimental data and retrieve the parameters
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 15
14
Step 3: implement the mathematical equation in COMSOL and perform the time-dependent simulation
Model results
Operational Point
Solar-driven CO2 reduction: Model
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 16
15
Solar-driven CO2 reduction: first results
Approx. J=3.35 mA/cm2
(Jmodel=3.4 mA/cm2)
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 17
Conclusions and Future Perspectives
16
A comprehensive model for the CO2 electro-reduction is proposed, validated through experimental results
The photovoltaics module is implemented through its governing equation
More complex electrochemical cells will be implemented (e.g. Flow Cells)
Optimize the model to be predictive for PV-EC performance under different incident light conditions (e.g. cloudy weather)
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 18
Thank you for your attention!
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 19
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 20
Experimental set-up
Batch cell + electrolyte recirculation
Catalyst: Ag NPs
Electrolyte: 0.1M
L1= 1.2 cm ; L2=0.5 cm
Nafion membrane
J: Current recorded for each Voltage applied and normalized on the catalyst surface area
FE: Figure of merit to determine the selectivity towards the production of the product of interest
Agliuzza et al, J. Phys. Energy (2024)

## Slide 21
Results #0: Cathode-Height dependancy
The y-dependancy can be safely ignored.
All the data are reported as the average across the cathode height.
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 22
Results #2: inflow velocity u0 @ L=0.25 cm
Dependancy on flow velocity is more pronounced on higher voltages. The reason is related to the fact that higher CO2 feed rates is more impactful when there are higher rates of carbon dioxide comsuption.
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 23
Results #3: L=0.25 cm , u0=0.067 m/s @ V= 3 V , 4 V
bulk
cathode
bulk
cathode
cathode
bulk
cathode
bulk
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 24
Results #2: inflow velocity u0 @ L=0.25 cm
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)

## Slide 25
Results #4: L=0.25 cm , u0=0.067 m/s
Onset of FECO > FEH2
Onset of FEH2>FECO
@ x= xcathode
@ membrane surface
Notes: J0=exchange current density, current density at zero overpotential. Mass transport limitation is given by a limit in the maximum current density j
Diffusion-migration-convectoin: um = mobility, u=velocity, phi=electrolyte potential
Nernst eq modifies Eeq away from standard conditions (c=1M)