## Slide 1: Modeling and Simulation of Transcutaneous Oxygen Transport
M. A. Almatrood1, B. D. Unluturk1 1. Institute for Quantitative Health Science and Engineering, Department of Biomedical Engineering, Michigan State University, East Lansing, MI, USA
We developed a partial differential equation (PDE)-based O2 transport model within a 3D multilayer skin structure inspired by Grossmann’s model [1] (Fig. 1a). FEM was then performed in COMSOL to simulate O2 transport based on this model. We focused on time-dependent behavior to replicate the experimental conditions in [2], where PtcO2 is measured under modulated PacO2 using either through local occlusion with blood pressure cuff or systemic hypoxia via hypoxia mask. A set of PDEs was used to describe the blood flow and O2 transport inside the capillaries and across each skin layer (Fig. 1b )
U. Grossmann, “Simulation of combined transfer of oxygen and heat through the skin using a capillary-loop model,” Math. Biosci., pp. 205–236, 1982.
V. Vakhter et al., “A Prototype Wearable Device for Noninvasive Monitoring of Transcutaneous Oxygen,” IEEE Trans. Biomed. Circuits Syst., pp. 323–335, 2023.
A finite element modeling to define the relationship between PaO2 and PtcO2 aimed to enhance measurement accuracy, improve clinical relevance, and enable more personalized patient monitoring.
Continuous, real-time respiratory monitoring is vital for managing chronic respiratory diseases, preoperative care, and critical care, where rapid hypoxia detection impacts outcomes. Transcutaneous O2 monitoring (PtcO₂) offers a noninvasive surrogate for arterial O2 partial pressure (PaO₂), the gold standard, but its use is limited by physiological variability and inconsistent correlation with PaO₂. To address this, we present a finite element modeling (FEM) framework to examine the relationship between PaO₂ and PtcO₂. By simulating physiological O2 transport through multilayered skin, the model reveals dynamic responses under blood flow occlusion and oxygen inflow changes. Results align with clinical observations, validating the model’s accuracy and supporting its potential for personalized monitoring. These findings demonstrate the value of computational modeling in improving PtcO₂ reliability, enabling continuous, real-time respiratory assessment in high-risk clinical settings.
Abstract
Methods
FIGURE 1. a) Cross-sectional unit volume of skin in Grossmann’s model. b) Human tests scenarios used in FEM studies
The simulated occlusions (left) showed an immediate response in PtcO2 levels, reflecting rapid physiological response to decreased perfusion. Post-occlusion recovery times (around 6 minutes) were consistent across scenarios, emphasizing delayed vascular and metabolic compensatory mechanisms.
Simulated oxygen reductions (right) displayed a slow and more prolonged decrease in PtcO2, indicating a gradual skin adaptation to less drastic oxygen deprivation. PtcO2 measurements responded well to the gradual recovery levels of PaO2 post-hypoxia, suggesting intrinsic physiological limits in restoring tissue oxygenation levels, emphasizing the critical need for timely clinical interventions irrespective of the initial severity of hypoxia.
Results
FIGURE 2. FEM results for PtcO2 with respect to time for systemic hypoxia (left) and local occlusion (right) for different PaO2 values
Notes: A finite element modeling (FEM) framework is presented to explore the intricate relationship between arterial O2 partial pressure (PaO2) and transcutaneous O2 partial pressure (PtcO2). By simulating physiological O2 transport through multiple skin layers, the model provides detailed insights into the dynamic responses of O2 levels under conditions of blood flow occlusion and O2 inflow variations. The results obtained closely correlate with clinical observations, validating the model’s effectiveness and offering a robust foundation for personalized transcutaneous O2 monitoring devices. These findings through the computational model significantly enhances the accuracy of transcutaneous O2 monitoring, facilitating continuous, real-time respiratory assessment. Such precise monitoring is vital in clinical scenarios involving chronic respiratory disorders, preoperative care, and critical care settings, where rapid and accurate detection of hypoxia significantly influences patient outcomes.