## Slide 1: Performance Enhancement of a Haptic Motor via 3D Multi-Physics Simulation
Lucy Hsia
Jiangsu Yucheng ELE CO.,LTD
Our approach utilizes a coupled 3D electromagnetic-structural transient analysis.
Key parameters—including coil turns, excitation current, and the magnet's remnant flux density (Br)—are defined to calculate the 3D Lorentz force. This force is applied as a time-dependent load in a structural transient simulation, directly solving for the vibrational response (displacement, velocity, acceleration) and fully capturing the electromechanical process.
1. Y. Chen, W. Zhang, J. Z. Bird, et al. A 3-D Analytic-Based Model of a Null-Flux Halbach Array Electrodynamic Suspension Device. IEEE Transactions on Magnetics, 2015, 51(11): 8300405. 2. S. Zhang, M. Wang, H. Zhou, et al. Structural Analysis and Optimal Design of a Mobile Phone Vibration Motor [J]. Machinery Design & Manufacture, 2020, (3).
A High-Fidelity Predictive Model from Electrical Signal to Vibration
Haptic motors are critical for immersive user experiences in consumer electronics (e.g., Touchpad , VR controllers). Traditional design methods, however, often rely on simplified models that fail to capture critical electromagnetic-structural couplings.
This study establishes a high-fidelity 3D Multiphysics transient simulation framework, accurately modeling the complete process from electrical input to vibrational output to enable precise performance analysis and enhancement.
Introduction
Methodology
Fig. 1. Spatial Distribution of the Magnetic Field
The high-fidelity model provided profound insights into motor performance: • Accurate Frequency Tuning: Parametric studies of the vibration mass and spring stiffness enabled rapid and precise configuration of the target resonant frequency (F0). • Full-Dimensional Force Coupling: The magnetic-solid mechanics coupling inherently accounted for force transmission in both vibrational and non-vibrational directions, revealing the complete 3D force state for superior simulation accuracy. • Optimized Transient Response: Simulation of various drive waveforms identified an optimal profile that achieved faster start-stop response times.
Results
Fig. 2. Simulated vs. Measured Acceleration Curve
(Measured: Green, Simulated: Blue)