## Slide 1
Corneal Epithelial Permeability and Permeability Measurement
Shashank Bharadhwaj1, Mohd. Danish Ahmed1, CSN Harshavardhan1, S P Srinivas2, Sudhir H Ranganath1
1Department of Chemical Engineering, Siddaganga Institute of Technology, Tumkur, India, 2Indiana University, Bloomington, IN, USA
Simulation of Measurement of Corneal Permeability by Multi-Drop Method using COMSOL Multiphysics
Results and Discussion
Conclusions
Objectives
Limitations of Measuring Permeability and Multi-drop method
Develop mathematical models of fluorescein transport across the human cornea
Simulate fluorescein transport across the human cornea in a novel multi-drop permeability measurement method
Compute corneal epithelial permeability using the parameters estimated via modeling
Mathematical Modeling of Fluorescein Transport across the Cornea
Fluorescein clearance in the tear film at any time is given by: _________ (1)
where, is the fluorescein clearance rate constant and is time.
Fluorescein partitions at the tear film-epithelium interface:
where, is the volume of the epithelium, KA is permeability, is the partition coefficient of fluorescein between the tear film and the epithelium, is the partition coefficient of fluorescein between the epithelium and the stroma.
Applying the boundary condition for transfer across the tear film-epithelium interface:
The equation reduces to:
To represent Fluorescein diffusion in the stroma,
Fick’s second law was used:
Figure 3: Multi-drop method for measuring corneal epithelial permeability (Pdc) using a custom-made spot fluorometer.
Concentration quenching
Inner filter effects
Low spatial resolution
Figure 2: Concentration quenching and inner filter effects seen in the measurement of Fluorescein concentration using a custom-made spot fluorometer.
Cornea: Barrier to pathogenic agents
Barrier integrity of epithelium determines the corneal health
Barrier integrity expressed in terms of permeability to Fluorescein
Permeability affected in dry eye disease, aging and diabetes
Conventional methods for measuring epithelial permeability
  Single drop method
  Bath technique
Estimated permeability < 100 times the expected values
Figure 2: Routes for fluid and drug transport across the corneal epithelium. Courtesy: https://upload.wikimedia.org
Figure 4: Schematic representation of Fluorescein concentration across the depth of the cornea
Depth of the Cornea (mm)
Tear film (~ 7 mm)
Epithelium (~ 50 mm)
Stroma (~ 500 mm)
Figure 5: Fluorescein clearance dynamics in the tear film in four normal human subjects. is obtained by fitting fluorescence intensity data vs. time.
kd (s-1) | D (m2/s) | (mol/m3) | s)
0.018 | 7.76 x 10-12 | 8.669 x 10-7 | 
0.018 | 1.5 x 10-12 | 1.5197 x 10-6 | 
0.006833 | 1.5 x 10-12 | 3.6846 x 10-6 | 
0.006833 | 7.76 x 10-12 | 2.0979 x 10-6 | 
kd (s-1) | D (m2/s) |  | 
0.018 | 7.76 x 10-12 | 8.669 x 10-7 | 
0.018 | 1.5 x 10-12 | 1.5197 x 10-6 | 
0.006833 | 1.5 x 10-12 | 3.6846 x 10-6 | 
0.006833 | 7.76 x 10-12 | 2.0979 x 10-6 | 
Experimentally determined value of corneal epithelial permeability: 0.01 to 1.28 nm/s
Fluorescein clearance from the tear film followed mono exponential decay.
Transport in the epithelium is a pseudo-steady state transport, while diffusion in the stroma is seen to be transient.
Results from the simulation yielded permeability value close to experimentally determined values in human subjects.
Values Obtained from the Simulation
KA(C0 - ) __________ (4)
KA(C0 - ) – KA( - C2) __(2)
Parameters | Symbol | Value | Unit
Initial Fluorescein concentration in the probe drop | C0 | 0.17 | mol/m3
Fluorescein clearance rate constant | kd | 0.12 | s-1
Diffusion coefficient of Fluorescein in the stroma | D | 7.76 x 10-12 | m2/s
Partition coefficient of Fluorescein in the tear film-epithelium interface | Ø10 | 0.556 | -
Volume of the corneal epithelium | VE | 7.952 x 10-13 | m3
Permeability | kA | 1.48 x 10-17 | m3/s
Parameters used in the simulation
Computation of Permeability after Simulation
Figure 1: Anatomy of the human cornea. The cornea is a three cellular layered tissue consisting of the outermost epithelium, middle stroma and the innermost endothelium. Courtesy: https://dreamstime.com
Acknowledgements
For more details, contact: Dr. Sudhir Ranganath at sudhirh@sit.ac.in, Phone: +91-9901699216
Sree Siddaganga Education Society, Tumkur for intramural research funding to Bio-INvENT Lab
Department of Chemical Engineering, SIT, Tumkur
Indiana University School of Optometry, Bloomington, IN, USA
Tear film
Epithelium
Stroma
Stroma
After the instillation of the probe drop
After the instillation of the loading drop
Loading Drop
Probe Drop
Stroma
Epithelium
Tear Film
Stromal accumulation after second loading Drop
Comparison of stromal accumulation
of fluorescein after the probe drop and
the first loading Drop
Tear film
Tear film
is the fluorescein elimination constant in the tear film
is the initial fluorescein concentration of the probe drop
is the stromal thickness
is area under the fluorescence vs. time curve for the loading drops.
and are proportionality constants for the calibration curve between tear and stromal fluorescence and fluorescein concentration.
and are mass of fluorescein in the probe drop and loading drop respectively, is the volume of the tear
is the average stromal fluorescence measured ~ 15 min after instillation of the second loading drop