## Slide 1
Design and Simulation of Indigenous Roll-over Sensor for Four-Wheeler Automobiles
Piyush Raj, Adarsh G Datta, Vishnu Kumar
Centre for Nano Science and Engineering, Indian Institute of Science, Bangalore, KA, India.
Advantages of this design:
Less sensitive to process variations
Less sensitive to operating conditions
High Bandwidth
Challenges:
On-chip detection needed
Conclusions: 4-DOF system offers superior performance compared to other systems. Careful calculation of operating frequency is crucial to robustness of design.
Introduction: Goal of our work is to design and simulate a 4-DOF MEMS vibratory gyroscope. Design has to be mechanically robust, compact, and durable since it is intended to be deployed in a life-threatening scenario.
References:
C. Acar, A. Shkel, "Structural Approaches to Improve Robustness," in MEMS Vibrating Gyroscopes, Springer, 143-144 (2008)
G. C. Y. G. G.Q. Wu∗, "A dual-mass fully decoupled MEMS gyroscope with wide bandwidth and high linearity," Elsevier, no. Sensors and Actuators A 259 50–56 (2017)
K. M. H. K. Masanori Yachi, "Development of a Roll Over Sensor," Fujitsu Ten Tech Journal, no. Fujitsu Ten Tech Journal, No (13), 1999.
Figure 1. COMSOL Multiphysics® design of 4-DOF MEMS Vibrating Gyroscope
Figure 3. (a) Spring constant calculation of serpentine structure
(b) Displacement of m1 with sinusoidal excitation
(c) Velocity of decoupling frame with sinusoidal excitation
(d) Capacitance variation with displacement amplitude of sense electrode attached to sense mass
Figure 2. Detailed look at the Gyro design
(a)
(b)
(c)
(d)
a = Fixed drive electrodes
b = m1 (6.4956e-9 kg)
c = m2 (3.41e-9 kg)
d = Fixed sense electrodes
e = k1x (6.667 N/m)
f = k2x (714 N/m)
g = k2y (714 N/m)
h = k3y (1.66 N/m)
i = m3 (5.087e-9 kg)
j = Drive electrodes on drive mass
k = Sense electrodes on sense mass
a
b
c
d
e
f
g
h
i
j
k
Results: Operating frequency = 70 kHz
Applied force = 16.48 µN (amplitude)
Sensitivity = ~10-15 F/(rad/s)