## Slide 1
The effect of viscosity on dynamics of Electrowetting droplet
Ning Weng
Qian Xuesen Laboratory

## Slide 2
Outline
Introduction
Mathematical Models
Results and Discussion
Conclusions

## Slide 3
Introduction
Digital microfluidics
Liquid lens
Micro switches
Optical valves and mirrors
Reflective displays

## Slide 4
Mathematical Models
Fluid properties and simulation conditions
Parameter | Symbol | Value | Unit
Density of liquid | ρl | 1000 | Kg/m3
Dynamics viscosity of liquid | μl | 0.0001,0.001,0.01,0.1,0.8 | Pa·s
Density of air | ρa | 1.204 | Kg/m3
Dynamics viscosity of air | μa | 1.814*10-5 | Pa·s
Surface tension | σ | 0.0712 | N/m
Droplet diameter | D | 1.016 | mm
Voltage | V | 120 | V
Initial contact Angle | θs | 118 | °
Thickness of dielectric layer | d | 5 | um
Relative permittivity of the insulating dielectric layer | εr | 3.15 | 
Hydrophobic layer(PTFE) | d | 100 | nm

## Slide 5
Mathematical Models
Navier-Stokes equations for fluid flow:
Moving mesh for interface

## Slide 6
Mathematical Models
θD
h
R
Fig 1. Schematic of electro-wetting droplet on a surface

## Slide 7
Mathematical Models
Liquid droplet
g
air
Open flow boundary
Open flow
boundary
z
r
Wetted wall
Fig 2. Schematic of computational domain

## Slide 8
Results and Discussions
Dynamics Process of Electro-wetting droplet(μl=0.001Pa·s voltage=120v)
20ms
50ms
10ms
1ms
3ms
5ms
7ms
6ms
9ms
Fig 3. Electro-wetting process of droplet on the substrate (V=120V, μl, =0.001 Pa·s)

## Slide 9
Results and Discussions
Fig 4. Time evolution of contact radius of droplet with different viscosity in DC (V=120V)
Fig 5. Time evolution of height of droplet with different viscosity in DC (V=120V)

## Slide 10
Results and Discussions
Fig 6. Time evolution of contact line velocity of droplet with different viscosity in DC (V=120V)
Fig 7. Time evolution of contact angle of droplet with different viscosity in DC (V=120V)

## Slide 11
Conclusions
The dynamic process of electrowetting droplet on solid substrates were simulated using Moving Mesh.
The MKT based dynamic contact angle model can be successfully used to numerical analysis of droplet dynamics.
When droplet’s viscosity is low, it recoils and undergoes damped oscillations under DC Electro-wetting. When droplet’s viscosity is high, oscillations don’t occurs.

## Slide 12
Thank you