## Slide 1
K.B. Dedey1,2,3*, T. Lucas1,2,3 , D. Grenier1,2,3
Stress Concentration Analysis in A Heterogeneous Dough Gas Cell Wall at The Microscale: the effect of gluten/starch interaction and rheological moduli ratio
1 Université Rennes 1, avenue du Général Leclerc, 35042 Rennes cedex, France
2 IRSTEA, UR OPAALE, 17 Avenue de Cucillé, CS 64427, F-35044 Rennes, France
3Université Bretagne Loire, France
dedeykossigan@gmail.com tiphaine.lucas@irstea.fr and david.grenier@irstea.fr
1.1 Governing equations
1-element generalized maxwell model
Linear viscoelasticity
Neo-Hookan visco-hyperelasticity (Incompressible material)
2.4 Stress concentration analysis: critical rupture spot within the GCW
2.1 Linear viscoelasticity vs visco-hyperelasticity
Figure 2: Mean of the Von Mises stress, comparaison between linear viscoelasticity and visco-hyperelasticity in the case of a. cohesive bond, b. non-cohesive bond at the gluten/starch interface.
2.2 Sensitivity analysis on strain rate and time of relaxation
2.3 Effect of gluten/starch rheological moduli ratio and interactions
(Quasi-static study)
1. Materials and methods
2. Results and discussion
3. Conclusions
References
Aknowledgements
[1] Sandstedt, R., The microscopic structure of bread and dough. Cereal Chem., 1954. 31: p. 43-49.
[2] Mohammed, M.A.P., et al., Mechanical characterization and micromechanical modeling of bread dough. Journal of Rheology, 2013. 57(1): p. 249-272.
[3] Ng, T.S., G.H. McKinley, and M. Padmanabhan, Linear to non-linear rheology of wheat flour dough. Applied Rheology, 2006. 16(5): p. 265-274.
[4] Kusunose, C., T. Fujii, and H. Matsumoto, Role of starch granules in controlling expansion of dough during baking. Cereal chemistry, 1999. 76(6): p. 920-924
[5]Sandstedt,R.M.1961.Thefunetionofstarehinthebakingofbread.Baker'sDig.35:36.
1.2 Geometry, boundary conditions and material properties
Material properties
Figure 1: Finite element model, geometry dimensions and boundary conditions.
Thin Elastic layer : cohesion/decohesion
Boundary conditions : unidirectional extention
(initial conditions)
= (displacement at the end of extension)
= 30 or 100% (strain)
Decohesion :
Cohesion :
(interface tickness)
Introduction : Understanding the gas cell wall (GCW) rupture behavior is crucial to control the specific volume and porosity of the bread. Between the end of the fermentation and the end of the baking the GCW must be considered as a heterogeneous material consisting mainly of gluten and starch granules [1,2].
Aim : Interactions between gluten and starch in GCW under unidirectional extension was modeled using linear viscoealsticity (small strain < 0.1) and visco-hyperelasticity (finite strain over 1).
GCW at the end of the baking. By Sandstedt [1]
Strain and strain rate range from begining of the fermentation to the end of the baking
()
=
Starch granule
Gluten film
The linear viscoelasticity describes material behaviors in low strain(<0.1)
The visco-hyperelasticity is more suitable for predicting GCW behavior in large strains > 0.3
Verified regardless of the nature of interactions between the gluten and the starch granule
No critical effect of the nature of gluten/starch interactions
Great effect of gluten/starch rheological modulus ratio
Strain hardening and strain softening were reproduced by the proposed model
Great sensitivity of the mean of Von Mises stress within GCW with respect to the ratio between the gluten and starch rheological moduli
This work was co-funded by Université Bretagne Loire (UBL, France) and the National Research Institute of Science and Technology for Environment and Agriculture (IRSTEA, France).
Non-cohesion
= 0.1
: low extensibility of the dough film which is more likely to rupture (Image a.)
: high extensibility of the film due to the relief of the gluten film by the starch (Image b.)
Linear viscoelastic model |  | Neo-Hookan hyperelastic model
 |  | = 1 or 10
 | 0.4999 | 
=3. |  | 
Linear viscoelastic model |  | Neo-Hookan hyperelastic model
 | 0.4999 | 
Strain hardening and softening behavior depended on strain rate [3]
Stress in GCW greatly depends on time of relaxation especially at small strain rate
The softening of starch granule (r<1) relieves stress concentration and increases ability of GCW to extend without rupture
The nature of the interactions at the gluten/starch interface shown no great effect on the mean of Von Mises stress within GCW for the considered gluten/starch proportion
Figure 3: Mean of the Von Mises stress within GCW, comparison of the proposed model to Filament Stretching Rheometry (FiSER) experiment on a strong flour dough by Ng, McKinley [3] for different relaxation times (𝜏𝑟= =1, 10, 100 𝑠 ) a. = 3.: strain softening and, b. = 3.: strain hardening ().
Figure 4: Mean of the Von Mises stress in the case of cohesion and non-cohesion at the gluten/starch interface for r<1 and r>1 ( = 3.).
Figure 5: The Von Mises stress concentration fields in the case of cohesion and non-cohesion at the gluten/starch interface for r<1 and r>1( = 3. and ).
(Small strains <0.1)
(Finite strains 0.1)
S : elastic stress tensor; 𝝉 : viscoelastic stress tensor
(the first invariant of the left Cauchy–Green tensor)
G: stress relaxation modulus function
: strain tensor
W: strain energy density function
: Young’s modulus in purely elastic spring
: Young’s modulus of the spring of branch 1
: Lamé coefficient (shear modulus)
: auxiliary stress tensor from thermodynamic consideration
: displacement vector
: strain tensor components
: strain energy factor
: isochoric part of second Piola-Korchoff stress
: volumetric part of second Piola-Korchoff stress
The set of equations was solved using COMSOL Multiphysics software
Bread dough strurture
  -The linear viscoelasticy was compared to the visco-hyperelasticity
  -The strain hardening, strain softening behaviors and sensitivity to the relaxation time were assessed in visco-hyperelasticity
  -The effect of gluten/starch rheological moduli ratio on Von Mises stress concentration within GCW was studied
  -Von Mises stress concentration analysis was performed to localize the spot where GCW is most likely to rupture
Gas cell wall
By Sandstedt [5]
By Kusunose, Fujii [4]
Early GCW rupture
Late GCW rupture
spring constant per unit area in directions normal and tangential respectively
: Young modulus at interface
relaxation time of material i : Poison’s ratio G : share modulus.
On the mean of Von Mises stress
Cohesion
Cohesion
Non-cohesion
= 10
a
b
a
b
a
b
∇. =
S =2 =+ +
Neo-Hookean model