## Slide 1: Fluid-Structure Interaction of Coupled Valves in Sucker Rod Pump
Shreyas V. Jalikop(a),
B. Scheichl(b), S.J. Eder(a,b)
(a) AC2T research GmbH, Austria
(b) Technical University of Vienna, Austria
Notes: 1
COMET - Competence Centers for Excellent Technologies
Das Programm COMET fördert den Auf- und Ausbau von Kompetenzzentren, deren Herzstück ein von Wirtschaft und Wissenschaft gemeinsam definiertes Forschungsprogramm auf hohem Niveau ist; das COMET Programm ist die Fortsetzung des Kompetenzzentrenprogramms Kplus.
COMET - Das Programm
Aufbau gemeinsamer Forschungskompetenzen zwischen Industrie und Wissenschaft
COMET - Programmlinien
Das Programm COMET umfasst 3 Programmlinien
K1 vs. K2
Kplus
Kplus-Zentren: Zusammenführung industrieller und wissenschaftlicher Kompetenz zu international konkurrenzfähigen "Centers of Excellence".

## Slide 2: Introduction
Down-hole pump
Oil reservoir
Down hole pumps
Most widely used type of pumps in oil industry
Usually more than 1000m underground
Scarce measurement data from pumps
Multiple damage mechanisms: corrosion, impact, etc.
Realistic pump operation hard to predict
Fluid dynamic related pump damage not well understood
www.omv.com

## Slide 3: Sucker-rod pump operation (ideal conditions)
Ideal pump-card
Schematic of down-hole pump
Opening/Closing driven by fluid forces
Fluid structure interaction (FSI)
OMV

## Slide 4: Model description
Computational model
Moving mesh (ALE)
Automatic remeshing (distortion)
6 boundary layer mesh
Assumptions of the model
SPF module : No turbulence: laminar flow (justified for force calculations)
2D axisymmetric flow
Single fluid phase model
Rigid pump components
COMSOL model
TP
PIP
Plunger kinematics
Boundary conditions
Imposed PIP & TP
Imposed plunger kinematics

## Slide 5: Computational challenges
Moving boundaries
  ALE module for moving mesh
  Automatic remeshing
Valve closure
  Avoided solid-solid contact
  Artificial repulsive force
Ball dynamics
  Implicitly solved using Global Equations node

## Slide 6: Computational challenges
Moving boundaries
  ALE module for moving mesh
  Automatic remeshing
Valve closure
  Avoided solid-solid contact
  Artificial repulsive force
Ball dynamics
  Implicitly solved using Global Equations node
Prescribed Mesh Velocity
(plunger speed)
Prescribed Mesh Displacement
(ball displacement)
TV Ball
SV Ball
Expanding
chamber
Seat
Seat

## Slide 7: Computational challenges
Moving boundaries
  ALE module for moving mesh
  Automatic remeshing
Valve closure
  Avoided solid-solid contact
  Artificial repulsive force
Ball dynamics
  Implicitly solved using Global Equations node
Artificial repulsive force model
: critical cut-off gap
: sensitivity parameter
Force is similar to …
Penalty factor in contact mechanics
Regularising force in elasto-hydrodynamic lubrication theory

## Slide 8: Computational challenges
Moving boundaries
  ALE module for moving mesh
  Automatic remeshing
Valve closure
  Avoided solid-solid contact
  Artificial repulsive force
Ball dynamics
  Implicitly solved using Global Equations node
Solves plunger kinematics
Solves ball kinematics
Coupled system of ODEs solved by Global Equations node

## Slide 9: Results (ideal pump card)
Partially open valves
SV
TV

## Slide 10: Ball dynamics (Net force)
Net force = (Drag due to fluid flow) – (weight of the ball)
Real
Ideal

## Slide 11: Ball dynamics (Net force)
Real
Ideal
Fluctuations in net force on the SV ball for actual pump card data due to fluctuations in plunger speed; whereas steady force on the ball in the ideal case
Zoom plot shows that net force goes below zero (indicating downward force on the ball) in regions where ideally it should be steady
These regions of negative net force can lead to mid-cycle valve closure!

## Slide 12: Valve opening
Real
Ideal
TV
SV
Mid-cycle valve closure is indeed observed!

## Slide 13: Valve opening
The valve closure correlates to a fluctuation in plunger speed
Real
Ideal
TV
SV

## Slide 14: Gap pressure
Seat
Ball
Gap pressure computed at the mid-distance of the shortest line joining the ball and the seat
Real
Ideal
TV
SV
Time dependent gap between ball and seat using General Extrusion
COMSOL Blog by Walter Frei

## Slide 15: Gap pressure
Real
Ideal
TV
SV
Mid-cycle valve closure results in a sudden pressure drop.
The first dip is due to the valve opening process, and is also present in the ideal case
This presents danger of gas/vapour formation
Possible root-cause of other know damage mechanisms. Eg. Gas intereference, fluid pound.

## Slide 16
m/s
N/m^2
Real
Ideal

## Slide 17: conclusion
First FE model for studying FSI of a pair of coupled ball check valves
Moving boundaries
  Implemented using ALE and Global Equations node
  Large variations (> 60 times) in geometry in time handled by COMSOL
Real case pumping scenarios can be simulated
The model is a helpful tool for pump design

## Slide 19
The topics presented are based on research projects carried out at the “Excellence Centre of Tribology” (AC2T research GmbH, Wiener Neustadt, Austria) with the support by the Austrian program (Project XTribology, no. 849109) and by the concerned program management institutions, viz the Austrian Research Promotion Agency (Österreichische Forschungsförderungs-Gesellschaft mbH), on behalf of the Federal Government, as well as by the Government of Niederösterreich, Wien, and Vorarlberg.
We are as well grateful to the involved company partners and scientific partners for their financial support and for the fruitful cooperation.
XTRIBOLOGY
ACKNOWLEDGEMENT

## Slide 20: Non-ideal pump operation
WC
Typical real pump-card
Pump/Valve
Damage
Damaged seat
Undamaged valve
www.downholediagnostics.com
A good model should capture non-ideal scenarios
Relative valve opening/closing states
Coupled valves model

## Slide 21: Dynamics of the valve balls
Artificial repulsive force model
: critical cut-off gap
: sensitivity parameter
Force is similar to …
Penalty factor in contact mechanics
Regularising force in elasto-hydrodynamic lubrication theory
Hydrodynamic drag and gravitational force
: hydrodynamic drag
(surface integral of stress in vertical direction)
: force due to gravity
Ref: COMSOL
Application ID: 12655
Ball dynamics

## Slide 22: Coupled equations for pump kinematics
Solves plunger kinematics
Solves ball kinematics
Coupled system of ODEs solved by Global Equations node

## Slide 23: Parametric study of critical plunger speed
Constant flow rate boundary condition
Drag
Partially open valve
Fully open valve
A constant flow rate was imposed
Simulation was carried out to find the final position of the ball starting from an almost closed valve
Critical plunger speeds (boundary between partial opening and full opening) for various ball densities were computed.

## Slide 24: conclusion
First FE model for coupled valves
  Fluctuation in plunger speed can lead to sudden pressure drop  danger of
    gas formation/cavitation and
    mid-cycle valve c
Constant flow rate simulations
  Boundary between partial and complete opening of valve

## Slide 25: Parametric study of critical plunger speed
Drag
A constant flow rate was imposed
Simulation was carried out to find the final position of the ball starting from an almost closed valve
Critical plunger speeds (boundary between partial opening and full opening) for various ball densities were computed.
Actual pump card data
Constant flow rate boundary condition

## Slide 26: Results (real pump card)

## Slide 27: Results (real pump card)

## Slide 28: Gap pressure
Seat
Ball
Gap pressure computed at the mid-distance of the shortest line joining the ball and the seat
Time dependent gap between ball and seat using General Extrusion

## Slide 29: Valve closure model

## Slide 30: Simulation flow chart
00
Simulation of fluid flow in down hole pump
Plunger motion
Liquid properties
Pump geometries
Opening/closing of pump valves
Hydrodynamic pressure and forces on ball and pump

## Slide 31: Plunger motion
Plunger motion
Any pump card can be given as input to the model
Ideal motion of the plunger can also be used for certain parametric studies

## Slide 32: Assumptions of liquid
Liquid properties
Constant density and viscosity of the liquid
Single phase of the fluid
Newtonian fluids

## Slide 33: Simplification from 3D to 2D
Pump geometries
3D
2D
Full 3D geometry is used to develop an equivalent 2D geometry that can approximately reproduce the hydrodynamic forces on the ball
Ball
Ball
Seat
Seat

## Slide 34: Real vs ideal pump card
Hydrodynamic pressure and forces on ball and pump
Opening/closing of pump valves
Real
Ideal
TV
SV
Real
Ideal
Force on the ball
Gap pressure
Mid-cycle valve closure

## Slide 35
m/s
N/m^2
Ideal pump card:
Real pump card (note the mid-cycle valve closure!):

## Slide 36: fixed Narrow gap simulations
Ball
Seat
Gap
Pressure field (Gap = 0.15mm, Plunger Velocity = 0.12m/s)
Pressure along the gap (Gap = 0.15mm, Plunger Velocity = 0.12m/s)
plunger velocity [a.u.]
gap width [a.u.]
Micro-bubbles?

## Slide 37: Parametric study of critical plunger speed
Constant flow rate BC
Drag
A constant flow rate was imposed
Simulation was carried out to find the final position of the ball starting from an almost closed valve
Critical plunger speeds (boundary between partially opening and fully opening) for various ball densities were computed.
Actual pump card data

## Slide 38: Seat failure via impact?
Depends on the Co-content (~9-14wt%) and the grain size of the microstructure (~1µm = “fine”)
For “low” impact velocity (~0.7 m/s)  unlikely
For “high” impact velocity (~1.3 m/s)  possible
  14wt% Co  transverse rupture strength ~3 GPa  ductile failure
  14wt% Co and fine microstructure  compressive strength ~4.5 GPa  brittle failure
Is Seat Failure via Impact Possible?

## Slide 39: The upshot
Can open/closed states of valves be self-consistently reproduced based on plunger kinematics?  yes
Can mid-cycle valve closure occur?  yes, if the plunger velocity drops below a critical value and the ball is too heavy
Can the associated pressure drop in the gap be enough to cause micro gas bubbles to form and collapse, causing damage outside of the ball/seat contact reagion?  yes, this seems likely
Is WC seat failure by pure mechanical impact possible?  For impact velocities >1 m/s: possible  this can be kept to a minimum by keeping the Co binder content between 8–14wt% and the grain size between 1–10 µm

## Slide 40: Possible studies and extensions
Possible studies using the current model
Simulate 3-4 commercially available cage geometries  differences?
  Suppression of mid-cycle valve closure  longer service life?
  Higher pump efficiency?
  Better valve opening/closing / more stable valve behaviour?
Calculate minimum plunger speed for several pump diameters
Possible extensions to the model
Simplified pump model
  Use detailed simulation results of the valves to build a lumped force model of the pump
Multi-phase flow
  Include effects of multi-phase fluid (e.g., water and oil)

## Slide 41: Sucker-rod pump operation (ideal conditions)
COMSOL Model
Ideal pump-card
Schematic of down-hole pump

## Slide 42: Ball dynamics (Net force)
Net force = (Drag due to fluid flow) – (weight of the ball)
Actual
Ideal

## Slide 43: Ball dynamics (Net force)
Fluctuations in net force on the SV ball for actual pump card data due to fluctuations in plunger speed; whereas steady force on the ball in the ideal case
Zoom plot shows that net force goes below zero (indicating downward force on the ball) in regions where ideally it should be steady
These regions of negative net force can lead to mid-cycle valve closure!
Actual
Ideal

## Slide 44: Valve opening
Mid-cycle valve closure is indeed observed!
Actual
Ideal
TV
SV

## Slide 45: Valve opening
The valve closure correlates to a fluctuation in plunger speed
Actual
Ideal
TV
SV

## Slide 46: Gap pressure
As expected, a mid-cycle valve closure results in a sudden pressure drop in the gap (second dip in the zoomed plot)
The first dip is due to the valve opening process, and is also present in the ideal case
This presents danger of gas/vapour formation
Real
Ideal
TV
SV