## Slide 1: Numerical Analysis of Bubble Powered Micropump
Gad A. Pinhasi
Matan Pe’er and Amos Ullmann
COMSOL CONFERENCE 2019
Cambridge, September 24–26

## Slide 2: Micro Pump
A lab-on-a-chip (LOC)
Micro Fluidic Pumps
  Insulin Pump (drug delivery)
Electronics cooling, Ink Printers, …
Micro-channels and Pump
(Lin and Tsai, 2002)
1mm
Active Mixer (Evans et al., 1997)

## Slide 3: Bubble Micro-Pump
Driving force
  Bubble formation, growth and collapse
  Vapor volume change
Flow control
  Diffuser/Nozzle
Unsteady Pumping flow
  Pulsing flow
No moving parts
Tsai and Lin (2002)
Jung and Kwak (2007)

## Slide 4: Bubble Lifetime Cycle
Heating
  “Waiting” Time
Bubble formation:
  Stable bubble criterion
  Nucleation
Bubble growth
  Inertia Controlled
  Diffusion Controlled
Collapse
Problem: Discontinuity in the flow field in time
Deniray and Kim (2004)

## Slide 5: The Objective
Developing a numerical model to simulate the operation of a micro-pump driven by bubble formation and growth.
Sub-models:
  Initial liquid heating,
  Formation of a critical bubble,
  Bubble growth and collapse
  The liquid flow through the nozzles system.

## Slide 6: Basic Assumptions
Laminar flow
Heating with constant heat flux.
  Duty cycle (= 80%)
Initial liquid temperature: Ambient
Initial Hemispherical critical bubble on the wall
Case Study:
  Displacement Pump: 2D, 3D analysis
  Bubble growth simulation: 2D spherical
  Bubble Pump: 2D analysis
q”
t
Tc
th
DC=th/Tc

## Slide 7: Conservation Equations
Continuity
Momentum: NS Eq.
Heat Eq.: Convection
Heat and Mass Transfer at the Boundary
  Phase Change
  Moving boundary
Vapor
Liquid
Heat
q”
Evaporation
me”

## Slide 8: Liquid-Vapor Boundary Representation
Level Set Method
  Fluid interface representation
  Level-set Parameter
  f [0,1], f=0.5
  Fixed Grid
f
RB
Vapor
Liquid
r
d
1
n
Interface

## Slide 9: Bubble Formation Criterion
Wall heating
  Semi-infinite body
  Constant heat flux
Critical Radius
Nucleation
Hsu (1962)
B
A
t
Heating
Plate
Bubble
RB
Liquid Heating
Critical Radius

## Slide 10
Liquid Heating Model
Bubble formation
Liquid
Liquid
Bubble Growth Model
Bubble Removal
Bubble Nucleation Criterion
Bubble Collapse Criterion
Yes
Yes
t+dt
No
t+dt
No
Heating surface
Interface formation
Bubble growth

## Slide 11: The CFD Tools
MATLAB Based
  Main program
  Script (MATLAB)
COMSOL Multiphysics
  Physics:
    Laminar flow
    Heat Transfer
    Fixed Grid Boundary problem: Level set
  Grid generator
  Solver
  Post Proceeding
COMSOL Multiphysics and the LiveLink for MATLAB
Combine user code and software functions and solvers:

## Slide 12: Results
Diffuser/Nozzle Characteristics
Displacement Pump
Bubble growth
Bubble pump

## Slide 13: Diffuser/Nozzle Characteristics
Steady state flow
Minor losses Coef.: K
Effectiveness h
  High h, directed flow
Diffuser Nozzle

## Slide 14: 3D Displacement Pump
v

## Slide 15: Spherical Bubble Growth
Bubble radius time history
3D Analysis
Axial symmetry
Comparison against analytical models
  Diffusion Controlled
  Inertia Controlled

## Slide 16: Bubble Pump
Boundary conditions
  Pressure drop
  Heater segment
Initial Conditions:
  Initial temperature: 298K
  Contact angle 90
  Hemispherical liquid domain
1 mm
1 mm
2 mm
0.3 mm
0.03 mm
0.18 mm
q”
t
T
th
DC=th/T
Heating
Plate

## Slide 17
  Bubble Growth Stage
  Velocity-Pressure map

## Slide 18: Velocity and flow rate
Net flow rate
  3.81E-7 [m2/s]
  9.14 [µl/min]
Bubble radius
Bubble Pump
Bubble Radius [m]
Time [s]
Heat Flux in = 1M [W/m2]
Bubble Growth R = 0.14mm
Bubble Collapse
Heat Flux out = 10k [W/m2]
Duty cycle = 80%
Time [s]
Net Flow Rate
[m2/s]

## Slide 19: Head and Efficiency
Bubble Pump

## Slide 20: Summery
A numerical model was developed to simulate the operation of a micro-pump driven by bubble formation and growth.
The model solves the time dependent conservation equation for viscid fluid: mass, momentum and convection heat transfer.
The Level-Set method is being used to represent the gas-liquid interface.
The analysis is made by using finite element software-COMSOL Multiphysics.
The model was tested against analytical model for diffusive bubble growth.

## Slide 21
Pinhasi, G.A., Pe'er, M. and Ullmann, A. (2019) “Numerical Analysis of Bubble Powered Micropump”, Proceedings of COMSOL Conference 2019, Cambridge, September 24–26.