## Slide 1
INTRODUCTION: In 2016 the group of experimentalists in the Institute of High Current Electronics has been discovered a new phenomenon: an extended stable plasma jet developing perpendicular to the bending point of the arc discharge channel (“apokamp”).
This phenomenon is of great interest as a novel object of theoretical investigation including the frameworks of deterministic modeling with uncertainties as well.
COMPUTATIONAL METHODS: The Plasma Module represents the hydrodynamic description of non-equilibrium gas discharges using the two-moment and drift-diffusion approaches:
RESULTS: Time-dependent numerical study is showed that the number of apokamp channels is determined by the applied voltage value. The arc channel bend ensures a local field enhancement, which determines the initial orientation of the growing streamer channels.
CONCLUSIONS: The theoretical model of apokamp discharge was developed. The model allows to explore the appearance and development of multiple apokamps in atmospheric-pressure chlorine at the wide range of applied voltage.
REFERENCES:
Bourdon et al., “Efficient models for photoionization …”, Plas. So. Sci. and Tech., 16, 656–678, (2007)
Hagelaar et al., “Solving the Boltzmann equation …” Plas. So. Sci. and Tech., 14, 722–733, (2005)
Sosnin et al., “Apokampic discharge: Formation …” Russian Physics Journal, 62, 1289-1297, (2019)
Sosnin et al., “Phenomenon of apokamp discharge”, JETP Letters, 103, 761-764, (2016)
Figure 1. Domain configuration
Figure 2. Plasma density distribution
The Numerical Simulation of Apokamp: A Novel Source of an Atmospheric-Pressure Plasma Jet
V. Yu. Kozhevnikov, A.V, Kozyrev, N. S. Semeniuk, A. O. Kokovin, and A.G. Sitnikov
Laboratory of Theoretical Physics, Institute of High Current Electronics SB RAS, Tomsk, Russia
Excerpt from the Proceedings of the 2020 COMSOL Conference
where ne and nε are the electron density and energy density respectively, ρ is the mixture density, ωk is the mass fraction of k-th species, Re is either a source or a sink of electrons, Rε is the energy loss or gain due to inelastic collisions, Rk is the rate expression of k-th species computed using the BOLSIG+ code.
Type of reaction | Reaction | Rate expression
Photoionization | hν + Cl2 → e + Cl2+ | Rph = S1 + S2 + S3
Impact ionization | e + Cl2 → 2e + Cl2+ | 5.12∙10–8∙Te0.48∙ exp(–12.34/Te)
Dissociative attachment | e + Cl2 → Cl + Cl– | Cross section was taken using the BOLSIG+ code
Detachment | e + Cl– → 2e + Cl | 2.63∙10–8exp(–5.37/Te)
Recombination | Cl– + Cl2+ → Cl2 + Cl e + Cl2+ → Cl + Cl | 5∙10–8 9∙10–8∙Te–0.5
Impact dissociation | e + Cl2 → e + 2Cl | 1.04∙10–7∙Te–0.29∙ exp(–8.84/Te)
Table 1. Reactions set in chlorine (rates in cm3/s). Electron temperature Te given in eV.
Photoionization process is described by three linear Helmholtz equations using the Coefficient Form PDE Interface of Mathematics Module:
where j = 1,2,3, λj, Aj and pq are constants defined in [1], pO2 is the partial pressure of molecular oxygen.
High-voltage electrode
t1/2 = 2.5 μs
U0 = 10–50 kV
Arc discharge channel
Floating potential electrode
Bright process
BCs:
2D computation domain
x
y
Ground
The building of user-controlled mesh in the area of apokamp channels is difficult due to the small channels width and their bend. Using the Adaptive Mesh Refinement option allows each apokamp channels to be resolved.
-4
-2
0
2
4
x-coordinate, mm
14
12
10
8
6
4
2
0
-2
-4
y-coordinate, mm
U0 = 50 kV
U0 = 25 kV
U0 = 10 kV
-4
-2
0
2
4
x-coordinate, mm
-4
-2
0
2
4
x-coordinate, mm
-4
-2
0
2
4
x-coordinate, mm
No ground