## Slide 1
Development of Simulation Model for Pyroclastic Flows using COMSOL Multiphysics®
Mauro Iacuaniello, Andrea Montanino, Daniela De Gregorio, Giulio Zuccaro

## Slide 2
CONTENTS
Volcanic risk,
Volcanic risk in the Neapolitan area,
Actions and effects on the buildings of the different volcanic phenomena,
Exposure assessment of the red and yellow areas of the Campi Flegrei and Vesuvius,
Vulnerability assessment,
Mitigation strategies,
Conclusions and perspectives

## Slide 3
INTRODUCTION TO THE VOLCANIC RISK
RISK = HAZARD x EXPOSURE x VULNERABILITY
HAZARD is the probability that, in a specific area, a specific event occurs during a specific time.
EXPOSURE is the extension, the quantity and the quality of different anthropic elements which characterize the examined area (population, buildings, facilities, etc.), whose conditions and/or functioning can be damaged, altered or destroyed by a volcanic event.
VULNERABILITY is the tendency of people, buildings, activities and property to show damage or changes under effect of volcanic events

## Slide 4
SOURCE: Department of Civil Protection
«Scenari Eruttivi e Livelli di Allerta per il Vesuvio» (2010)
REFERENCE SCENARIO: VESUVIUS AND CAMPI FLEGREI
SOURCE: Department of Civil Protection
«Scenari Eruttivi e Livelli di Allerta per Campi Flegrei» (2012)
the formation of a sustained eruptive column 12 km high and with a total erupted mass of 1,2 e11 kg;
the fall of volcanic bombs and blocks in the immediate vicinity of the crater and smaller particles (ash and lapilli) even several tens of kilometres away;
the formation of pyroclastic flows that would flow along the slopes of the volcano for several kilometres.
the formation of a sustained eruptive column 18 km high and with a total erupted mass of 5.0 e11 kg;
the fall of volcanic bombs and blocks in the immediate vicinity of the crater and smaller particles (ash and lapilli) even several tens of kilometres away;
the formation of pyroclastic flows that would flow along the slopes of the volcano for several kilometres.

## Slide 5
ACTIONS AND EFFECTS
SOURCE: Spence R., Zuccaro G., Petrazzuoli S., Baxter P.J., (2004b). The resistance of buildings to pyroclastic ﬂows: theoretical and experimental studies in relation to Vesuvius.
EARTHQUAKES (EQ)
PYROCLASTIC FLOWS (PF)
ASH FALL (AF)
LAHAR (LH)
Horizontal and vertical cyclic action proportional to masses
Damage to structures and/or non-structural elements
Non-cyclical impact surface action (0.5-17 kPa),
Thermal stress (150/400 °C).
Damage to structures and/or non-structural elements,
Opening up,
Fire damage inside.
Uniform vertical static pressure on roofs
Collapse of the roofing slabs
Non-cyclical impact surface action (20/90 kPa),
Temperature effect (<100°C).
Damage to structures and/or non-structural elements especially on the ground floor

## Slide 6
EXPERIENCE IN MONSERRAT
Effects of pyroclastic flows
Photo by Peter Baxter

## Slide 7
TYPOLOGICAL AND STRUCTURAL IDENTIFICATION OF ELEMENTS EXPOSED TO RISK
LARGE
TYPICAL
SMALL

## Slide 8
(A)
(B)
(C)
para = range (0,0.1,10)
FL = 1[kN/m] * para
1. Solid Mechanics
Applied load
comp1.StressMax > 40[MPa]
Stop Condition
Geometrical model :
Fixed Constraint, B) External Front,
C) Symmetry condition
MECHANICAL ASSESSMENT
Density | 2700 [kg/m3]
Elastic modulus | 70000 [MPa]
Ultimate Stress | 160 [MPa]
Poisson Coefficient | 0.33
Specific heat capacity | 900 [J/kgK]
Thermal conductivity | 238 [W/mK]
Thermal expansion | 3,7 e-7 [1/K]
Aluminium EN-AW 6060 (Thermal Break)

## Slide 9
Frame |  | Aluminium | 
Glass |  | Soda Lime | 
Large |  |  | 
4mm | 5mm |  | 6mm
0,6 kPa | 1 kPa |  | 1,3 kPa
Typical |  |  | 
4mm | 5mm |  | 6mm
2 kPa | 3 kPa |  | 4,3 kPa
Small |  |  | 
5,3 kPa | 8 kPa |  | 10,33 kPa
MECHANICAL ASSESSMENT: BREAK LOAD

## Slide 10
2. Thermal Stress
Applied temperature
Heat transfer in solid
Thermal expansion
Geometrical model :
Fixed Constraint, B) External Front,
C) Symmetry condition
THERMAL ASSESSMENT
(A)
(B)
(C)

## Slide 11
Maximum temperature of polyamide and EPDM
Maximum temperature of soda-lime glass
Von Mises stress
THERMAL ASSESSMENT

## Slide 12
1. Thermal Stress
2. Solid Mechanics
Applied temperature
Heat transfer in solid
Thermal expansion
para = range (0,0.1,10)
FL = 1[kN/m] * para
Applied load
comp1.StressMax > 180[MPa]
Stop Condition
MECHANICAL AND THERMAL ASSESSMENT

## Slide 13
Thermal stress for 4- and 6-millimeter glass
Break load for 4- and 6-millimeter heated glass
MECHANICAL AND THERMAL ASSESSMENT
Maximum temperature of polyamide

## Slide 14
= + K] + F (4.1)
= 0
Inlet
Outlet
= 25 m/s
1. Turbolent Flow (k-)
2. Nonisothermal Flow
FLUID DYNAMICS ASSESSMENT

## Slide 15
Velocity
Temperature
FLUID DYNAMICS ASSESSMENT

## Slide 16
Maximum temperature of polyamide and EPDM (CFD)
FLUID DYNAMICS ASSESSMENT

## Slide 17
PERSPECTIVES

## Slide 18
THANK YOU FOR YOUR KIND ATTENTION
© Stromboli online · J. Alean · R. Carniel · M. Fulle