## Slide 1
INTRODUCTION: An experiment was set-up to reconstruct the migration of hydrocarbon-leaks, occurring on the earth´s surface and subsurface. Examples includes buried pipelines and underground storage tanks, from where leakages discharge.
COMPUTATIONAL METHODS: A time and space-dependent saturation equation is proposed, to clearly track the LNAPL saturation front. For the crude-oil and diesel fluids comprised in the porous system, a combination of continuity equation and Darcy law were solved simultaneously for both system-phases wherein either saturation or pressure, were considered as primary variable.
(2)
Mapped mesh was used instead of triangular mesh. Five elements are used in r-direction while 2000 element were used in z-direction.
RESULTS: Experiments in 2D axisymmetric, 3D, and the saturation propagation of LNAPL, at different time steps, are presented in Figs. 3 and 5. Fluid flow behavior due to soil subsurface characteristics is shown in Fig.6 as fingering.
CONCLUSIONS: The numerical model successfully tracked the LNAPL capillary imbibition and saturation fronts, its robust matching with the laboratory results was a good validation for our experimental model.
REFERENCES:
Onaa, C., Nassan, T. H., & Amro, M., Experimental and numerical evaluation of diffusivity influence on hydrocarbon fluids capillary imbibition – Environmental study. European Oil and Gas Journal. 6. https://doi.org/10.19225/200603 (2020)
Hopmans, J. W., Grismer, M. E., & Chen, J. (n.d.). Parameter Estimation of Two-Fluid Capillary Pressure- Saturation and Permeability Functions (1998)
Nassan, T. H., & Amro, M, Finite Element Simulation of Multiphase Flow in Oil Reservoirs -COMSOL Multiphysics as Fast Prototyping Tool in Reservoir Simulation. Mining Science and Technology. https://doi.org/10.17073/2500-0632-2019-3-220-226 (2020)
Onaa, C., & Amro, M. M, Comparative investigation of vapor expulsion technique (VET: Via N2-treatment) and carbonate-clay based adsorbents as sustainable approaches for oil-leak remediation. Environmental Technology & Innovation. https://doi.org/10.1016/j.eti.2020.101062 (2020)
Figure 2. The axisymmetric domain with fine mesh.
Figure 3. Diesel saturation front in 20-hours of imbibition
Figure 4. Laboratory model of imbibition
Figure 5. Plot of saturation model showing (a) upwards diffusion and (b) downward diffusion of diesel after 20 hours of imbibition.
Figure 1b. Schematic illustrastrating the saturation of model-sand, from the Centre of the profile.
C. Onaa, T.H. Nassan, M.M. Amro
Excerpt from the Proceedings of the 2020 COMSOL Conference
Figure 6. Simulation model illustrating crude-oil Fingering and vaporization behaviour.
Figure 1a. Conceptual model
(a)
(b)
Institute of Drilling and Fluid Mining Engineering, Freiberg University of Technology and Mining – Germany
Corresponding author contact: onaa@mailserver.tu-freiberg.de
Experimental and Numerical Simulation of Light Non-aqueous Phase Liquids Imbibition in Unconsolidated Porous Media