## Slide 1: Modeling of charged droplet dynamics in an Electric Field using COMSOL Multiphysics®
14th October 2020
M. STURMA1, P.NAMY2, V. BRUYERE2, and B. BARBET1
1. MARKEM-IMAJE Industries BP110 26501 Bourg-Lès-Valence France 2. SIMTEC, 5 rue Felix Poulat 38000 Grenoble France

## Slide 2
Markem-Imaje
30 subsidiaries and 180+ partners
6 industrial platforms
250 R&D employees
3,000 employees
5 centers of excellence
7 coding technologies
50,000 customers worldwide
Laser
Impression pose
étiquettes
Logiciels
Consommables
Jet d’encre
Global manufacturer and distributor of specialized traceability and product identification equipment, for customers in the packaging industry.

## Slide 3: Continious Inkjet (CIJ) technology
Droplet generator
Charge electrode
Deflexion electrode
Ink recycling
Gutter
Gutter
direction of displacement of the printing media (bottle, paper, wire …)
Perturbation signal
The printing quality depends on drop position determined by:
++ the drop charge
++ the electrostatic field
+ unwanted drops interaction in flight
(electrostatic repulsion and aerodynamic effects).
Goal of the numerical study :
compute droplets trajectory to predict droplet positions on the media
Droplet diameter:
Jet velocity: 20m/s
 100 000 drops/s

## Slide 4: 2D COMSOL model
Charge electrode
Deflection electrodes
Media
Meshing :
184,399 nodes

## Slide 5: Step 1: Electrostatic study
On other boundaries E
V=4300V
Ground
V= 0 V
Stationary study

## Slide 6: Step 2: Charged particule tracing study
Charged particule/electrostastic field interaction
-
-
-
Charged particule/particule interaction
Coulomb force
(N-1)² interaction
Lorentz force
Droplet Solid particles of ink

## Slide 7: Particule x-axis position
Z=1.93pC
Z=0.48pC
x
x
Electrostatic interaction
 x-deviation
No interaction
 Ballistic flight
x
-

## Slide 8: Raster (48 droplets) deviation

## Slide 9
Experimental
8,46 mm
8,4 mm
Numerical
Deflection amplitude: correct order of magnitude
Same trend for the local gap between droplet
Droplet positions are not exactly identical wake effect
Comparaison with experimental data

## Slide 10: Conclusion & perspectives
2D model coupling an electrostatic study and a charged particles tracing study (weak coupling)
Simulation of the trajectory of charged droplets rasters into our print head
the repulsion between charged droplets is taken into account
High level of confident thanks do the comparaison with analytical model and experimental data
Adding wake effect
by strongly coupling this model to a NS calculation to get the air velocity distribution around each droplet