## Slide 1
1. E. Westby, “Macromodelling of Microsystems”, 2004.
2. H. V. Allen et al;. “Accelerometer systems with self-testable features,” Sensors and Actuators, 1989.
Cross Domain Modelling of a Meander Beam MEMS Bulk Micromachined Accelerometer in COMSOL Multiphysics® and SPICE
Mahdieh Shojaei Baghini1
1. Delft University of Technology, Delft, Netherlands
Excerpt from the Proceedings of the 2020 COMSOL Conference
Introduction
Fig. 1. Eight-beam Si accelerometer with squeeze film damping fabricated using anisotropic wet etching.
Static and dynamic modelling of MEMS accelerometers using COMSOL and lumped circuit elements enables cross domain design, analysis and simulation of these devices. Meander beams are utilized due to their lower effective vertical stiffness as compared to rectangular beams and placed at the edges of the proof mass to reduce parasitic frequencies which lead to tilts [1,2].
SPICE Analytical Model
Computational Model
The force applied on the proof mass is modeled by a current source. Consequently, each discrete element models a mechanical variable, conserving energy. The damping is modeled by R and L. The damping ratio
(ζ) is 0.7.
Results
Fig. 2. Lumped element circuit model of accelerometer with thin film damping.
Solid mechanics physics is used for the derivation of proof mass displacement, eigen modes, damping factor and resonance frequency of accelerometer ().
Fig. 3. Distribution of finer
mesh elements at beam-mass interface.
Transient modelling
Eigen-frequencies modelling
Wall height for thin film damping is derived previously using SPICE models based on desired damping factor.
The sensor exhibits a stable transient response on application of a body load. The presence of parasitic frequencies leading to tilts in the proof mass is highlighted by the higher order eigen modes. As acceleration increases, the SPICE derived displacement diverges from that of COMSOL since validity of small deformation theory is not satisfied.
Fig. 3. First eigen mode corresponding to the natural frequency.
Fig. 4. Third eigen mode corresponding to the second parasitic frequency.
Color bar: Surface displacement (μm)
Fig. 5. SPICE and COMSOL simulated proof mass displacement vs acceleration.
Conclusion
First four eigen modes of designed meander and rectangular beam MEMS accelerometers.
The placement of meander beams away from the center leads to a reduction of parasitic effects and off-axis sensitivity. The drop in resonance frequency causes an increase in the damping factor of the sensor.
As the beams are moved
towards the center, operation
bandwidth reduces.
In order to improve
performance,
closed loop capacitive
accelerometers can be
designed with feedback.
References
The author would like to thank Dr. Andre Bossche for his valuable inputs.
Acknowledgements
COMSOL = 1.1
SPICE = 0.7
f0COMSOL = 1.454 kHz
f0SPICE = 1.575 kHz