## Slide 1
REFERENCES:
1. Xiaorong, & Xu. Conformal Cooling and Rapid Thermal Cycling in Injection Molding With 3D Printed Tools. (1999).
2. Agazzi, A. Contribution à l’optimisation de la thermique des outillages dans le procédé d’injection des polymères thermoplastiques (2011).
Figure 3. Preheating temperature profiles on the AB segment at
Figure 1. Dilated zone created around the piece. (Conformal approach)
Heat transfer optimization in hybrid manufacturing processes involving high performance composites using COMSOL MULTIPHYSICS® and Livelink® for Matlab
Excerpt from the Proceedings of the 2020 COMSOL Conference- 14, 15 October2020
Enrique Reyes Rodriguez (1,2), Xavier Tardif (1), Jean-Luc Bailleul (3), Nadine Allanic (3), Vincent Sobotka (2)
(1)IRT Jules Verne, Chemin du Chaffault, 44340 Bouguenais; (2) Nantes université, CNRS, Laboratoire de thermique et énergie de Nantes, LTeN, UMR 6607, F-44000 Nantes; (3) Laboratoire de Génie des Procédés–Environnement–Agro-alimentaire (GEPEA) UMR CNRS 6144, Nantes
A
B
A
Top Side
Botton Side
Introduction: An inadequate temperature control, during forming of High Properties Thermoplastic Composites (HP-TC) , could not only lead to mechanical and surface defects but also to an inefficient energy consumption. These problems become difficult to avoid with the interaction of different materials within the part, and also with the influence of subsequent stages on the process.
As part of the Project PERFORM, conducted by the IRT Jules Verne, this work aims to describe how to determine the spatial and temporal distribution of the heat sources that must be applied during different stages of a forming process to reach a thermal objective within the part. To do this, a thermal design methodology that could be adapted to different manufacturing processes of HP-TC is proposed based on the concept of conformal cooling [1] and on an inverse optimization method.
The conformal approach proposes the creation of contour (dilated zone) reproducing the shape of the part, as close as possible to the mold’s surface [1], where heat fluxes are searched.
Figure 1. Hybrid manufacturing process stages
on
o
Direct problem
Sensivity problem
Adjoint problem
• The proposed algorithm can effectively obtain improved heat flux conditions in comparison with a trial-error simulation. Maximum profile temperature at the top of the surface goes from 15°C à 6.5°C and form 18°C to 7°C at bottom.
• The optimization process allows us to take the optimized condition in one stage as the initial condition for the next stage in the process.
• Further analysis will include experimental validation and constrained optimization based in process requirements.
A
B
A
B
Zone in contact with the insert
Target
Melting point
Figure 4.Transfert temperature profiles on the AB segment at
Figure 5. Stamping and overmolding temperature profiles and the end of each stage
Figure 6. Temperature profile distribution after optimization
The analysis is focused only on the heat transfer. A 2D axysimetric, incompressible and non-deformable system is considered with contact thermal resistances between all the domain parts (insert, composite, polymer, tools)
This allows us to create only a dilated zone[2] around the part, instead of the entire mold to analyze the heat transfer, reducing computational time and separating the process from the actual physics.
Metal insert
(Aluminium)
Dilated zone
(Steel)
Overmolding
(PEEK)
Organosheets
(PEEK+ Carbon fiber)
Uniform temperature distribution
Target temperature
3
a)
b)
d)
Hybrid manufacturing process
global exchange coeff(Insert/Composite*)
/ = Shape factor
c)
Figure 2. Boundary conditions: a) Preheating, b) Transfer, c) Stamping, d) Overmolding.
Results: Profile temperature distribution
6
Conclusions
7
Gradient
Descent
Cost Fonction
Gradient  descent direction
:
Deepest descent
Update
Initialization:
Solve Direct Problem
Evaluate Cost Fonction
<
Optimal
no
yes
Conjugate gradient algorithm
Solving equations
4
Boundary Conditions
1
Approach and Computation model
2
5
3
Zone in contact with the insert
Zone in contact with the insert
Zone in contact with the insert
B
A
G
F
A’
B
A
B
F
G
A
A’
Target
Radiation and convection exchanges
Convection
Conduction
Conduction
Conduction
Convection
Confidential. Reproduction/ communication of all or part of this document is prohibited © IRT Jules Verne and the Laboratory thermal and energy of Nantes/ University of Nantes
Notes: Note:
All abstracts, papers, posters, and presentations must comply with, and are subject to, our Copyright Notice:
www.comsol.com/conference/copyright-notice
Reproduction/communication of all of part of this document is prohibited IRT Jules Verne