## Slide 1: Multi-Physical Simulation of Aerostatic Bearings
F. Colombo, L. Lentini, T. Raparelli, A. Trivella, V. Viktorov
Department of Mechanical and Aerospace Engineering
Politecnico di Torino,Turin (Italy)

## Slide 2: OUTLINE
INTRODUCTION
  Aerostatic Pads
  Aim of This Study
MATERIALS AND METHODS
  Experimental Set-up
  Numerical Model
RESULTS AND DISCUSSIONS
CONCLUSIONS

## Slide 3: OUTLINE
INTRODUCTION
  Aerostatic Pads
  Aim of This Study
MATERIALS AND METHODS
  Experimental Set-up
  Numerical Model
RESULTS AND DISCUSSIONS
CONCLUSIONS

## Slide 4: OUTLINE
INTRODUCTION
  Aerostatic Pads
  Aim of This Study
MATERIALS AND METHODS
  Experimental Set-up
  Numerical Model
RESULTS AND DISCUSSIONS
CONCLUSIONS

## Slide 5: INTRODUCTION AEROSTATIC PADS: APPLICATIONS
Machine Tools
Measuring Machine
Power Board Testing
Aerostatic pads are widely used in applications where high precision is required, e.g.:

## Slide 6: INTRODUCTION AEROSTATIC PADS: FEATURES
PROS:
Low Friction
Low Wear
Limited Heat Generations
Long Life
Excellent Start-Up Performance
Aerostatic pads are characterized by:

## Slide 7: INTRODUCTION AEROSTATIC PADS: FEATURES
Their performance depends on many geometrical and physical parameters, e.g.,
Supply Pressure
Type, location and number of restrictors
Shape of the bearing land
Manufacturing
Deformations
…

## Slide 8: INTRODUCTION AEROSTATIC PADS: FEATURES
Their performance depends on many geometrical and physical parameters, e.g.,
Supply Pressure
Type, location and number of restrictors
Shape of the bearing land
Manufacturing
Deformations
…
The relevance of some of these aspects is
not taken into account in numerical models!

## Slide 9: INTRODUCTION AEROSTATIC PADS: FEATURES
The aim of this study to evaluate to what extent the accuracy of numerical models can influenced by some of these “secondary” aspects:

## Slide 10: INTRODUCTION AIM OF THE STUDY
The aim of this study to evaluate to what extent the accuracy of numerical models can influenced by some of these “secondary” aspects:
Tilting

## Slide 11: INTRODUCTION AIM OF THE STUDY
The aim of this study to evaluate to what extent the accuracy of numerical models can influenced by some of these “secondary” aspects:
Tilting
Concavity of the Bearing Land

## Slide 12: INTRODUCTION AIM OF THE STUDY
The aim of this study to evaluate to what extent the accuracy of numerical models can influenced by some of these “secondary” aspects:
Tilting
Concavity of the Bearing Land
Deformations

## Slide 13: INTRODUCTION AIM OF THE STUDY
The aim of this study to evaluate to what extent the accuracy of numerical models can influenced by some of these “secondary” aspects:
Tilting
Concavity of the Bearing Land
Deformations
Combination of the previous ones

## Slide 14: EXPERIMENTAL SET-UP THE AEROSTATIC PAD
Figure: Scheme of the bearing land.
Figure: Photograph of the bearing land.

## Slide 15: EXPERIMENTAL SET-UP THE STATIC TEST BENCH
Figure: Scheme of the static test bench
Static Characterization of the pad
Load Capacity (F vs h)
Air Consumption (G vs h)

## Slide 16: NUMERICAL MODEL PHYSICAL DESCRIPTION OF THE PROBLEM
The model consist of the bearing can be divide in different regions that have to be described through different types of flow models:
Feed Region (Euler’s equation)
Entrance Region (Boundary layer theory)
Viscous Region (Reynolds’ equation)
Figure: Main regions of the bearings.

## Slide 17: NUMERICAL MODEL PHYSICAL DESCRIPTION OF THE PROBLEM
The model consist of the bearing can be divide in different regions that have to be described through different types of flow models:
Feed Region (Euler’s equation)
Entrance Region (Boundary layer theory)
Viscous Region (Reynolds’ equation)
The more common solution consist in using an equilibrium pressure that links the inertial and the viscous region neglecting the growth of the boundary layer through the entrance region
Figure: Film flow configuration.

## Slide 18: NUMERICAL MODEL MAIN EQUATIONS
Figure: Main regions of the bearings.
Feed Region (Euler’s equation)
Viscous Region (Reynolds’ equation)

## Slide 19: NUMERICAL MODEL MAIN EQUATIONS
Feed Region (Euler’s equation)
Viscous Region (Reynolds’ equation)
1-3 Continuity equation

## Slide 20: RESULTS AND DISCUSSIONS TILTING
Figure: Numerical and experimental load capacity curves
Figure: Numerical and experimental air consumption curves

## Slide 21: RESULTS AND DISCUSSIONS TILTING
Figure: Comparison between the pressure distributions of the simulated pad

## Slide 22: RESULTS AND DISCUSSIONS DEFORMATIONS
Figure: Pad deflection in the presence of an air gap height of 5 m.
Figure: Numerical and experimental load capacity curves

## Slide 23: RESULTS AND DISCUSSIONS DEFORMATIONS
Figure: Pad deflection in the presence of an air gap height of 5 m.
The effect of the pad deflection in not negligible, especially in the presence of small air gap heights!

## Slide 24: RESULTS AND DISCUSSIONS DEFORMATIONS & CONCAVITY
Figure: Numerical and experimental load capacity curves
Figure: Numerical and experimental air consumption curves

## Slide 25: RESULTS AND DISCUSSIONS CONCAVITY
Figure: Experimental profile of the pad.
The presence of concavity was experimentally verified.

## Slide 26: CONCLUSIONS
This paper has presented a numerical and experimental investigation on some of the main parameter that can compromise the accuracy aerostatic pad numerical models: shape of the bearing land (concavity/convexity), tilting and deformations.
It was found that the theoretical tilting has no effect on the pad performance.
Conversely, the shape of the bearing land and the deflection exhibited by the pad significantly compromise the accuracy of numerical predictions.