## Slide 1
INTRODUCTION: Theoretical simulation of gas breakdown development has difficulties due to a wide range of initial conditions, under which gas breakdown occurs, a large number of species and plasma-chemical reactions, and the physical mechanisms that are extremely complex for experimental diagnostics and theoretical description.
COMPUTATIONAL METHODS: The Plasma Module represents the hydrodynamic description of non-equilibrium gas discharges using the two-moment and drift-diffusion approaches:
RESULTS: Time-dependent numerical study allows to obtain the detailed spatio-temporal characteristics of discharge, such as plasma components distribution, electric field, full current etc.
CONCLUSIONS: The theoretical model of positive corona discharge was developed. The model allows to study the breakdown development in detail. The minimal plasma-chemical reactions set and algorithms for describing the charged particles kinetics of air plasma were developed.
REFERENCES:
Bourdon et al., “Efficient models for photoionization …”, Plas. So. Sci. and Tech., 16, 656–678, (2007)
Hagelaar et al., “Solving the Boltzmann equation …” Plas. So. Sci. and Tech., 14, 722–733, (2005)
Pancheshnyi et al., “Development of a cathode-directed streamer …” Phys. Rev. E, 71, (2005).
He et al., “Modeling Study on the Generation of Reactive Oxygen …”, Plas. Proc. and Pol., 9, (2012).
Figure 1. Domain configuration
Figure 2. Plasma density distribution
Theoretical Simulation of Positive Corona Discharge in Atmospheric-pressure Air
A. O. Kokovin, A.V, Kozyrev, V. Yu. Kozhevnikov, and V. S. Igumnov
Laboratory of Theoretical Physics, Institute of High Current Electronics SB RAS, Tomsk, Russia
Excerpt from the Proceedings of the 2020 COMSOL Conference
where ne and nε are the electron density and energy density respectively, ρ is the mixture density, ωk is the mass fraction of k-th species, Re is either a source or a sink of electrons, Rε is the energy loss or gain due to inelastic collisions, Rk is the rate expression of k-th species computed using the BOLSIG+ code.
Ground
rcurv = 100 μm
Plasma channel
Tip
Air
1 atm
2D Axisymmetric
computational domain
U0 = 10 kV
d = 1 cm
BCs:
r
z
Reaction | Rate expression | Reference
Photoionization hν + O2 → e + O2+ | Rph = S1 + S2 + S3 | 1
Impact ionization e + N2 → e + e + N2+ e + O2 → e + e + O2+ | Townsend coefficients were calculated using the BOLSIG+ code | 2
Electron attachment e + O2 + O2 → O2 + O2– | 1.9∙10–30∙(0.026/Te)∙ exp[(1 – 0.026/Te)∙7/3] | 3
O4+ production O2 + N2 + O2+ → N2 + O4+ | 2.4∙10–30 | 3
Three-body recombination N2 + O2– + O4+ → N2 + 3O2 N2 + O2– + O2+ → N2 + 2O2 | 2∙10–25 | 3
Impact dissociation e + O2 → e + O + O | 4.2∙10–9∙exp(-5.6/Te) | 4
Table 1. Minimal reactions set (units of two-body reaction rates – cm3/s, three-bodies – cm6/s). Electron temperature Te given in eV.
Photoionization process is described by three linear Helmholtz equations using the Coefficient Form PDE Interface of Mathematics Module:
where j = 1,2,3, λj, Aj and pq are constants defined in [1], pO2 is the partial pressure of molecular oxygen.
The plasma channel structure consists of two areas: ionization area (“corona glow”) near the tip in form of thin (≈ 0.2 mm) jet and streamer propagating from corona glow towards the grounded electrode.
t = 43.6 μs
t = 43.4 μs
t = 42.5 μs