## Slide 1
INTRODUCTION:
Short-circuit faults exceed the nominal current of a system (up to ten times [1]) put the system at risk
The Superconducting Fault Current Limiters (SFCL) can protect the system from damage
SFCL’s impedance is negligible under normal operation and it rapidly increases when a fault occurs (Figure 1), reducing the current flowing through it and protecting the system
METHODS:
The SFCL is modeled as a superconducting tape, constituted of silver, REBCO, and Hastelloy
A 1-D thermal model (ht) coupled with an electric circuit (ec) (parallel resistors) is solved (Figure 2)
The REBCO's resistivity is modeled with the power-law model (characterized by the n-value: the higher the n, the steeper the characteristic)
RESULTS:
Analyzing the plots provided (Figure 4), the students will have to adjust the parameters (Figure 3) according to simple design criteria for the tape: Is the tape safe or burnt (Figure 5)?
CONCLUSIONS:
The App enables students to quickly enter the world of superconductivity and simulation methods, understanding the role of superconductivity, and the design criteria of a simple but important device such as a SFCL.
Figure 1. It is impossible to avoid short-circuit currents [2,3].
Teaching future engineers about superconductors
for power applications with an App
Nicolò Riva1, Francesco Grilli2 ,Bertrand Dutoit1
1. SCI IC BD, Ecole Polytechnique Fédérale de Lausanne (EPFL), Lausanne, Switzerland
2. ITEP, Karlsruhe Institute for Technology (KIT), Karlsruhe, Lausanne
Excerpt from the Proceedings of the 2020 COMSOL Conference
Figure 2. (left) Schematic circuit and (right) representation of the tape.
Figure 5. Dialog box illustrating if the tape is (left) safe or (right) burnt.
Figure 3. Snapshot of the App and (right) figure of merit calculated by the App.
GOAL:
A COMSOL App can help students learning how to deal with such complex concepts in a simplified and engaging format
By varying the circuit's design parameters and the tape, the goal is to keep the temperature of the tape below 450 K
What is Superconductivity?
Ask me in the chat or check
out this three minutes video!
Curious about this App any many other COMSOL models for superconducting applications?
REFERENCE
[1] Tixador P. Superconducting Fault Current Limiter
[2] Plane, Scott County (MN) Sheriff's Office Press Releases
[3] Squirrel, Yellow Blue Tech
Figure 4. (top) Limited and prospective current and (bottom) temperature profile during cooling of the REBCO material
Resistance
Low Imp.
High Imp.
Current