## Slide 1
Challenges of DC insulating systems for airborne applications
D. Anagnostou, C. Willich, J. Kallo
COMSOL 2020 Europe

## Slide 2: Electrification of Aircrafts
Aircraft electrification is progressing rapidly
Application in propulsion & subsystems (e.g. hydraulic, pneumatic)
Increased power demand leads to higher voltages of the powertrain.
Voltage level predicted to reach 3 kV DC in the near future

## Slide 3: Electric Field Distribution
|E| has different characteristics for AC and DC voltages
Variable operating conditions of the system:
  mixture of AC and DC field distribution or shift from one to the other
  fast and big temperature variations
AC, transients
Capacitive
D=εE
Not variable
AC, transients
Capacitive
Not variable
DC
Resistive
J=σE
Variable
DC
Resistive
Variable

## Slide 4: Electrical Conductivity of Insulators
Depends on:
Temperature
Pollutants – large molecules/particles
Radioactivity
High energy particles
Electric field strength
σair ≈ 10-14…10-15 S/m
[1]. Qin, S. & Boggs, S., “Design considerations for high voltage DC components“, IEEE Electrical Insulation Magazine, 2012, 28, 36-44
Temperature
Dependence
El. Field
Dependence
[1]

## Slide 5: Simulation Model
For the simulation was used:
Electric Currents (ec) interface from AC/DC Module
Heat Transfer in Solids (ht) interface from Heat Transfer Module
A Time Dependent study
The model parameters were:
Rduct =8,45mm
Rcond =5,25mm
Thicknessins=1,2 mm
Voltage = 1000V DC
Cu
Insulator
Air
Shield
Duct

## Slide 6: Electric Field Dependence
The |E| is low
 does not affect the value
of σins
The electrical conductivity of a solid insulator becomes a F(T)
Chart: Radial Position (mm)
NFD: No Field Dependence

## Slide 7: Thermal Gradient vs |E| Distribution
Small thermal gradient across insulator leads to:
linear change of field strength within the insulator
more uniform field distribution within the insulator
Chart: ΔΤ = 10°C
Chart: ΔΤ = 30°C
* A: 0,98eV activation energy, B: 0,56eV activation energy
Temperature difference between the inner and the outer side of the insulator of a shielded cable

## Slide 8: Unshielded Cable in Duct
The distribution of |E| changes over time in the insulator and the air
Cu
1000 V
80°C
Air 70°C
σair = 3x10-15 S/m
Insulator
at 0sec
after 20.000sec
Duct
0V

## Slide 9: Radial |E| Distribution
According to the operating and ambient conditions, the |E| distribution can vary significantly
Chart: σair = 3x10-15 S/m
Chart: σair = 8x10-15 S/m
* A: 0,98eV activation energy, B: 0,56eV activation energy
ins.
air

## Slide 10: Summary
The risk for partial discharges can be reduced by:
Using proper insulating materials
Improving the thermal design of the system
The |E| distribution around a cable under DC voltage was simulated and investigated
The comparison was done for:
  A shielded and an unshielded cable
  Two different types of the insulating material
  Two different values of σair
  Different conductor and air temperatures
This research was funded by the German Federal Ministry for Economic Affairs and Energy under the grant number 20Y1701B

## Slide 11
THANK YOU
for your
ATTENTION !