## Slide 1
INTRODUCTION: In the framework of the Greek-German co-operation project “Solar Collectors with Static Concentrators” (SCoSCo) a novel concentrating mirror array collector (MAC) design was established. It is based on a mirror array unit that was introduced earlier [1] but was modified from flat to focussing.
GEOMETRY: Figure 1. shows the geometric configu-ration of the MAC. All mirrors are pre-oriented and can be tracked in a coupled mode by two drives.
Figure 3. Optimal tube positions for different incidence angles
COMSOL MODELING (GEOMETRIC OPTICS MODULE):
The optical error and the solar cone angle of ±4.65 mrad were programmed together as part of the reflection condition on the mirror surfaces.
Figure 2. Complete setup of the COMSOL raytracing model inclu-ding ray source, mirror array, receiver box and virtual background surface,
EVALUATION: The intercept data of a range of incidence angles in x and y directions were used to calculate incidence angle modifiers (IAM) as input for the solar-thermal performance calculations using the Matlab/Simulink toolbox CARNOT [2].
An off-centre shift of the intensity distribution was found at oblique angles of incidence, which can be corrected by the MAC control algorithm.
CONCLUSIONS: Raytracing simulations were performed with respect to a novel concentrating solar collector design. The results confirm the feasibility of a coupled movement of the mirror facets using only two mechanical drives with acceptable optical losses. Good results can be obtained even when optical errors of ± 7 mrad are present.
Acknowledgements
This project was co-funded by the German Federal Ministry of Education and Research (BMBF) and the Hellenic Secretariat for Research and Technology (SCOSCO project) in the framework of the Greek-German co-operation.
Figure 5. Receiver intensity distribution at normal incidence (300,000 rays)
Figure 6. Intensity distribution of rays that pass between the mirror gaps
Figure 7. Intensity distributions for 30° f(left) and 30 °/40 ° (right)
IMPLEMENTATION: The mirror array was programmed using the COMSOL application builder so that the number and size of mirrors and the gaps between them could be varied easily (Fig. 2).
Multi-Mirror Array Calculations With Optical Error
J. Goettsche 1, S. Alexopoulos 1, A. Duemmler1 , S.K. Maddineni²
Solar-Institut Jülich, FH Aachen, Juelich, Germany
2. FH Aachen, Juelich, Germany
Figure 3. Reflected rays for 30° incidence angle
REFERENCES:
[1] Sauerborn, M. et al. 2008. Test of a Mini-Mirror Array for Solar Concentrating Systems, EUROSUN 2008, Lisbon, Portugal.
[2] CARNOT Toolbox Ver. 7.0 for MATLAB/Simulink R2018b, Solar-Institut Juelich
Figure 1. Sketch of the Mirror Array Collector (MAC)
Figure 4. Test of the reflection condition using a single 1mm² mirror left: solar cone only, centre: ± 1 mrad optical error with normal distribution, right: combination of both
RESULTS: The intercept factor (fraction of emitted rays that hit the receiver) and intensity distribution on the receiver were calculated for numerous parameter sets and angles of incidence. Near-optimal results were found with this parameter set.
Receiver size | Mirror facets | Concentration factor | Focal length | Optical error | Intercept (100,000 rays)
20 cm x 20 cm | 14 cm x 14 cm 7 x 11, gap: 1 mm | 38.2 | 1.4 m | 7 mrad | 88.3 %