## Slide 1
INTRODUCTION: Laser-induced forward transfer (LIFT) is a non-contact direct-write technique for high-resolution patterns usable for transferring high-viscosity metallic pastes [1, 2].
COMPUTATIONAL METHODS: The model is implemented as a 2D-axisymmetrical Two-Phase Flow, Phase Field interface. The movement of the fluid is induced by including a flow inlet that follows a predefined pressure function. The acceptor may be also included to study their influence.
RESULTS: The results has been compared to former works [1] in which silver paste LIFT images were taken. The different regimes have been replicated using this model: non-transference, dot-transference, explosive regime, and columnar structures [3].
CONCLUSIONS: The morphology and dynamics of the process is more understandable after its analysis through the numerical simulation of the process, under lower uncertainties for certain parameters that may fluctuate in the experiments, such as the paste layer thickness.
ACKNOWLEDGMENTS: This research has been funded by Spanish MINECO projects CONTACTOS SELECTIVOS Y CAPAS ACTIVOS PARA DISPOSITIVOS DE ENERGIA (SCALED) (PID2019-109215RB-C44) and CHENOC (ENE2016-78933-C4-4-R) and Comunidad de Madrid Projects ADITIMAT-CM (S2018/NMT-4411) and BIOPIELTEC-CM (P2018/BAA4480)
REFERENCES:
Munoz-Martin, D., Laser-induced forward transfer of high-viscosity silver pastes, Applied Surface Science, 366, 389-396 (2016)
Chen, Y., Laser Induced Forward Transfer of High Viscosity Silver Paste for New Metallization Methods in Photovoltaic and Flexible Electronics Industry, Physics Procedia, 83, 204-210 (2016)
Shan, Y., Laser direct printing of solder paste, AIP Advances, 9, 125306 (2019)
Simulation of laser-induced forward transfer for high-viscosity pastes
J. Moreno-Labella, M. Morales, D. Munoz-Martin, C. Molpeceres
Centro Láser, Universidad Politécnica de Madrid, Alan Turing 1, 28038, Madrid, Spain
Excerpt from the Proceedings of the 2020 COMSOL Conference
Figure 1. Title of the figure
Donor
Material
Acceptor
LIFT set-up
Inlet
Paste
Acceptor
Figure 1. LIFT setup
Figure 2. Pressure function (left) and initial geometry (right)
Figure 3. Non- transference regime
Figure 4. Dot transference
Figure 6. Columnar structure
Figure 5. Explosive regime